## Slide 1: WF on analysis of V2X RRM requirement
CATT
3GPP TSG-RAN WG4 #91 R4-1905368
Reno, USA, 13th May – 17th May, 2019

## Slide 2: WF on analysis of V2X RRM requirement for RAN4#92
Sidelink transmit timing error consists of:
  GNSS receiver timing error
  UE internal timing error
For GNSS based synchronization
  The sidelink transmit timing error is defined as 12*64Tc at least for 15KHz SCS
  FFS for other SCS
  Introduce the requirement for GNSS signal reliability
  For gNB based synchronization
  The sidelink transmit timing error can reuse the UL transmit timing requirements defined in TS38.133 section 7.1.2.
  Wait for RAN1’s decision on eNB-based synchronization source
  For Sync-Ref UE based synchronization
  Wait for RAN1’s decision on NR V2X sidelink physical layer design
Other RRM requirements is not precluded if identified.