## Slide 1: Way forward on NR mobility enhancement
Intel
3GPP TSG-RAN4 Meeting #91
Reno, USA, 13 – 17 May, 2019
R4-1905922
Document for: Approval

## Slide 2: Agreements on handover with simultaneous Rx/Tx with source and target cells
Handover from one frequency range to another with simultaneous Rx/Tx is feasible.
Handover with simultaneous Tx and Rx with both source and target cells involving different SCS is feasible depending on UE capability.

## Slide 3: Agreements on RACH-less handover
RACH-less handover with 0 or equal TA is feasible in FR2 with restriction on network deployment and low MCS scheduling. However, network needs to configure multiple UL grant resources associated with different DL RS (SSB or CSI-RS).

## Slide 4: Agreements on conditional handover
Handover delay in CHO is update by changing the starting point to the time when handover conditions are met.
DCHO = Tinterrupt + Tmeas_cycle
Where:
Tinterrupt: is the interruption time during handover procedure. The existing Tinterrupt in TS38.133 can be reused except the starting point is changed to the time when UE actually executes the handover.
Tmeas_cycle: is the measurement delay uncertainty, which can be up to 1 measurement cycle.