## Slide 1: WF on NR MIMO OTA
CAICT, Spirent, vivo, Apple, SGS
3GPP TSG-RAN WG4 Meeting #91 R4-1906111
Reno, Nevada, 13 - 17 May 2019
Agenda item: 10.2.1
Document for: Approval

## Slide 2: Channel model implementation
  System layout, RMS or weighted RMS spatial correlation error per R4-1706668 based on the agreed channel model should be provided
    CE vendors are encouraged to use the non-simplified channel model as the baseline, further simplifications are not precluded.
  Spatial correlation evaluation for system design
    The spatial correlation is evaluated between the origin and locations within a circular disc centred at the origin and having the radius of 10cm. The maximum spacing to be evaluated is 10cm. (i.e. Option 5 in R4-1906829)
    Spatial correlation sampling grid
      Rectangular
      Dx=Dy=0.1*l
    Spatial correlation validation testing procedure is FFS.
  Channel model implementation analysis is encouraged to be shared in the NR MIMO OTA reflector for discussion and alignment before next RAN4 meeting.

## Slide 3: Test Methods
  The measurement distance for FR1 MIMO OTA is at least 2l from the edge of the test zone.
  Radiated validation procedure of DL signal quality (e.g. EVM) per-port is required as starting point for FR1 MIMO OTA.
    Power level in the center of the test zone should be sufficient
  Orientations for FR2 MIMO OTA static testing
    Rotating DUT during the testing shall be adopted for FR2 NR MIMO OTA. How to rotate the DUT is FFS.
    Study how to choose potential test directions while considering the number of test points.
    Study feasible SNR ranges for FR2 MIMO OTA testing.

## Slide 4: Environmental conditions
  The Environmental condition:
    FR1:
      Option 1: UE noise-limited;
      Option 2: Interference-limited;
      Option 3: Hybrid condition;
    FR2: noise-limited environment is the baseline test. Interference-limited environment is not precluded.
  Further study the environmental conditions for FR1, the goal is to select only one environmental condition for FR1 NR MIMO OTA.

## Slide 5: NEXT actions
Ripple test procedure for FR1 and FR2 with 20cm
FR1 UE Orientation diagram in Annex A.3
TP on Channel model tables and scaling procedure
System layout for FR1 and FR2 should be provided