## Slide 1: 3GPP TSG-RAN WG4 Meeting #91 Reno, USA, May 13th – 17th, 2019
Huawei, HiSilicon
Way forward on UE sidelink timing requirements for NR V2X
R4-1906522

## Slide 2: Agreements on UE sidelink timing requirements for NR V2X
UE timing error requirement for gNB as time reference:
  Reuse the existing WAN requirements as defined in Table 7.1.2-1 of TS 38.133
UE timing error requirement for eNB as time reference:
Frequency Range | SCS of SSB signals (KHz) | SCS of uplink signals (KHz) | Te
1 | 15 | 15 | 12*64*Tc
 |  | 30 | 10*64*Tc
 |  | 60 | 10*64*Tc
 | 30 | 15 | 8*64*Tc
 |  | 30 | 8*64*Tc
 |  | 60 | 7*64*Tc
2 | 120 | 60 | 3.5*64*Tc
 |  | 120 | 3.5*64*Tc
 | 240 | 60 | 3*64*Tc
 |  | 120 | 3*64*Tc
Note 1: Tc is the basic timing unit defined in TS 38.211 |  |  | 
Downlink Bandwidth (MHz) | Te
1.4 | 24*TS
3 | 12*TS
≥5 | 6*TS
Note: TS is the basic timing unit defined in TS 36.211 | 

## Slide 3: Agreements on UE sidelink timing requirements for NR V2X
UE timing error requirement for NR UE as time reference:
UE timing error requirement for GNSS as time reference:
Frequency Range | SCS of S-SSB signals (KHz) | Te
1 | 15 | 12*64*Tc
 | 30 | 8*64*Tc
 | 60 | 6*64*Tc
2 | 60 | 6*64*Tc
 | 120 | 3.5*64*Tc
Note 1: Tc is the basic timing unit defined in TS 38.211 |  | 
Frequency Range | Te
FR1 | 6*64*Tc
FR2 | 3.5*64*Tc
Note: Tc is the basic timing unit defined in TS 38.211. |