## Slide 1: DSS in B41/n41
R4-1907060
Sprint

## Slide 2: Options in the Way forward in R4-1902968
Option 3: From Rel-16, the UE mandatory support the UL 7.5kHz shift and 100kHz channel raster. Reuse band n41 and introduce support for DSS
  DSS support: UL 7.5kHz shift, 100kHz channel raster
  Deploy SSB at SS raster positions where Rel-15 UE can not find it to prevent Rel-15 UE from accessing spectrum sharing NW
  It’s FFS whether Rel-16 UE mandatory supporting DSS
    For optional case, behavior of UEs that do not support DSS needs to be clarified
Option4: Reuse band n41, introduce support for DSS and use the cell barring mechanism to prevent Rel-15 UE to access band n41 cell with 7.5kHz UL shift configuration.
  Need to check feasibility from signaling perspective
  DSS support: UL 7.5kHz shift, 100kHz channel raster
  It’s FFS whether Rel-16 UE mandatory supporting DSS
    For optional case, behavior of UEs that do not support DSS needs to be clarified
Option5: From Rel-16, the UE mandatory support the UL 7.5kHz shift and Define a new band and UL 7.5kHz shift is mandatory supported in this new band
  The UE supporting new band shall also support band n41
  Apply all n41 requirements including CA and EN-DC band combinations (i.e. CA, DC, SUL) to new band
  Mandatory support of 100kHz channel raster is FFS

## Slide 3: Proposal from April RAN2 meeting
R2-1903207 Proposal for LTE/NR spectrum sharing in Band 41/n41 KDDI Corporation discussion NR_newRAT-Core
- Softbank think this is still being discussed in RAN4.
- ZTE think RAN4 are trying to resolve how to resolve this is a backwards compatible way such as define a new band or defining some chunks of the band 41 where the new requirements apply.
- KDDI think that new band and applying new requirement on existing band are discussed in RAN4.
- ZTE think it is not a RAN2 discussion so we need to wait for RAN4.
- Nokia explain that as the WI is Rel-16 in RAN4, it is release independent and that is why it comes to R15.
=> Wait for RAN4 progress before concluding what to do.
R2-1903208 The UE behavior correction for LTE/NR spectrum sharing KDDI Corporation CR Rel-15 38.331 15.4.0 0991 - F NR_newRAT-Core

## Slide 4: Why we feel operators should not be too concerned about legacy UEs causing UL interference
A new UE capability that indicates support for the 7.5 kHz UL shift can be used by the network to prevent EN-DC operation with the NR UL shift for UEs that do not support the UL shift
The earliest UEs likely won’t support Stand Alone NR operation, so minimal if any risk of “legacy” UEs accidentally transmitting RACH without the 7.5 kHz UL shift

## Slide 5: Proposal for B41/n41 spectrum sharing
Modified Option 4: Reuse band n41, introduce support for DSS and use the cell barring mechanism to prevent Rel-15 UE to access band n41 cell with 7.5kHz UL shift configuration.
  Need to check feasibility from signaling perspective
  Cell barring based on new tdd-frequencyShift7p5khz IE in the SIB
  DSS support: UL 7.5kHz shift, 100kHz channel raster
  It’s FFS whether Rel-16 UE mandatory supporting DSS
    For optional case, behavior of UEs that do not support DSS needs to be clarified
  DSS support is mandatory in Rel-16 with capability signalling
    New UE capability introduced to indicate support for 7.5 kHz shift, 100 kHz raster
    When 7.5 kHz shift is indicated in the SIB, a UE that does not support the shift considers the cell barred