## Slide 1: WF on RRM Requirements for HST
Ericsson
3GPP TSG-RAN WG4 Meeting #91 R4-1907091
Reno, Nevada, USA, 13th – 17th May 2019
Agenda Item: 6.10.10.1

## Slide 2: Way Forward: General
Specify RRM requirements (new or existing) for HST in Rel-15, provided HST performance requirements are also specified in the same release;
  At least in TS 38.133 is impacted,
  TS 36.133 may be impacted in case HST is supported for EN-DC or NE-DC
Add a note in the requirements applicability section clarifying the applicable bands and frequency ranges (e.g., all non-SDL and non-SUL frequency bands FR1)
Rel-15 NR RRM requirements for HST are specified (new or existing) for SA NR only without CA and without inter-RAT

## Slide 3: Way Forward: Measurements and Accuracy Requirements
UE measurement capability for HST is the same as for general Rel-15 NR UE, including:
  the number of frequency layers,
  reporting criteria,
  the number of measured cells and beams
Clarify all requirements sections applicable for HST in the requirements applicability section (section 3.6); further requirements details for HST, including configuration restrictions, can be captured in the relevant sections
Existing cell reselection, cell identification, and measurement requirements can apply also for UE configured with HST measurements, under additional conditions, e.g.,
  SMTC and SSB periodicity do not exceed 20 ms,
  CSI-RS periodicity (for beam management and RLM) does not exceed 20 ms
The existing Rel-15 NR measurement accuracy requirements apply also for HST propagation conditions

## Slide 4: Way Forward: RRM Test Cases
No RRM test cases will be specified for NR HST in Rel-15