## Slide 1: WF for NR-U Band plan work
Ericsson, ...
3GPP TSG-RAN4 Meeting #90bis
Reno, NV, USA, 13-17 May 2019
R4-1907100

## Slide 2: Background
It has been agreed that RAN4 will refarm band 46 as NR band n46 for NR-U usage in 5GHz range.

## Slide 3: Way forward for 5GHz range
Agreement on NR-U bandplan and channelization for 5GHz range
  No subbands should be defined for band n46
  For UE conformance testing, 5350-5470 MHz is exempt from testing.
  Define 10MHz, 20MHz, 40MHz, 80MHz CBW for band n46.
  The NR-U channel access structure in 5GHz spectrum for Type B multi-carrier transmission shall follow ETSI BRAN spec EN 301 893.

## Slide 4: Way forward for 6GHz
Agreement on NR-U bandplan for 6GHz range
  Specify a band for unlicensed usage within 5925-6425MHz spectrum.