## Slide 1: Way forward on UE demodulation enhancement for HST
Qualcomm Inc,...
3GPP TSG-RAN WG4 Meeting #91 Reno, USA, 13th May – 17th May, 2019
R4-1907164

## Slide 2: WF on extension of demod requirements to CA
Specify HST-SFN CA requirements based on Rel.14 train speed (350km/h)
  Ericsson, Qualcomm, NTT DOCOMO, CMCC
Not Define HST-SFN CA requirements
  Intel, MTK
Note: Chairman note in last meeting stated, “the WID does not preclude the discussion or introduction of HST-SFN CA demodulation performance requirements.” To align with extension of RRM requirements to CA and also in agreement with carriers that have HST deployments, CA requirement should be specified.

## Slide 3: WF on HST-SF scenario
Option 1: HST-SFN bi-directional scenario (Huawei, CMCC, Intel, NTT DOCOMO, Qualcomm, MTK)
  Two options of maximum Doppler
    Option 1: 1100Hz
    Option 2: 972Hz
  MCS options from 12 to 16
    (Qualcomm) select MCS 13 for 972Hz maximum Doppler
Option 2: HST-SFN uni-directional scenario (Ericsson, Qualcomm)
  Maximum Doppler shift for downlink for uni-directional
    Option 1: 1250Hz (Qualcomm)
    Other options with lower values compared to above not precluded
FFS: whether both bi- and uni-directional scenario are specified or not.

## Slide 4: WF on Additional Test to be Introduced
Option 1(NTT DOCOMO): add tests for HST single tap and multi-path with 500km/h speed, only applicable to UEs without enhanced HST-SFN capability
Option 2(Qualcomm): add test for only HST single tap with 500km/h speed, only applicable to UEs without enhanced HST-SFN capability
Option 3(Intel, MTK): do not specify additional tests

## Slide 5: WF on Transmission Mode
Transmission mode for test to be added:
  TM3
    Qualcomm, Intel, MTK, Ericsson, NTT DOCOMO,CMCC
  DMRS-based TM in addition to TM3
    Huawei
      Interested companies to further discuss the potential benefits, impacts and solutions for DMRS-based transmission
  NOTE: the proposed base station frequency compensation scheme is not feasible due to implementation complexity and accuracy of UE Doppler shift estimation, and the potential benefit is limited by DMRS overhead and the absence of CSI feedback