## Slide 1: Way forward on Noc and Es values for FR1 UE demodulation performance requirements
Intel
3GPP TSG-RAN4 Meeting #91
Reno, USA, May 13 - 17, 2019
R4-1907193
Document for: Approval

## Slide 2: Agreements
Capture the methodology to derive the minimum Noc and Es values for different bands for FR1 in 38.101-4
Use the fixed Noc and Es values for the FR1 UE demodulation performance requirements for bands and band combinations defined in release-15
  Noc = -134 dBm/Hz
  Es = -112 dBm/Hz
  Other Noc and Es values can be used for new bands and band combinations defined in the future depending on RAN4 analysis, if the minimum Noc and Es levels for new bands and band combinations exceed the fixed Noc and Es values used in Rel-15.
Use same Noc and Es values for each CC for normal demodulation and SDR requirements for CA and EN-DC scenarios

## Slide 3: Minimum Noc value
Methodology to derive the minimum Noc value for different bands for FR1
  Use a per-band minimum Noc power level
  Minimum Noc is at least X dB higher than UE RF noise floor for each band
    Noc (dBm/Hz) = PNoiseRF (dBm/Hz) + X dB
    X = 16 dB + allowance for CA band combinations and future bands
      16dB is chosen to give 0.1dB SNR degradation from Reference point to UE baseband
      allowance for CA band combinations and future bands currently expected to be 1.76dB
    PNoiseRF = REFSENS(Band_X, SCS_Y, CBW_Z) – 10*log10(BW) + D – SNRREFSENS
    REFSENS(Band_X, SCS_Y, CBW_Z) is the REFSENS value in dBm for Band X, SCS Y and CBW Z specified in TS 38.101-1 [Table 7.3.2-1]
    BW is useful bandwidth of signal, which is equal to 12*SCS_Y*nPRB
    nPRB is the maximum number of PRB for SCS Y and CBW Z specified in TS 38.101-1 [Table 5.3.2-1]
    D is diversity gain equal to 3 dB
    SNRREFSENS is -1 dB

## Slide 4: Minimum Es value
Methodology to derive the minimum Es value for different bands for FR1
  Use a per-band minimum Es power level
  Minimum Es is at least Y dB higher than UE RF noise floor for each band
    Noc (dBm/Hz) = PNoiseRF (dBm/Hz) + Y dB
    Y = 35 dB + allowance for CA band combinations and future bands
      allowance for CA band combinations and future bands currently expected to be 4.76dB
    PNoiseRF is same as for Noc calculation