## Slide 1: 3GPP TSG-RAN WG4 Meeting #91 Reno, USA, 13 – 17 May, 2019
Huawei, …
Way forward on General part of NR BS demodulation performance
R4-1907239

## Slide 2: Background
The following WFs were approved:
  R4-1808022 Way forward on general part for NR BS demodulation requirements, RAN4#87
  R4-1809370 Way forward on general parameters for BS demodulation performance requirements, RAN4#AH1807
  R4-1811726 Way forward on general part of NR BS demodulation performance, RAN4#88
  R4-1813755 Way forward on NR BS demodulation general part, RAN4#88Bis
  R4-1816346 Way forward on NR BS demodulation general part, RAN4#89
  R4-1902438 Way forward on General part of NR BS demodulation performance, RAN4#90
  R4-1904715 Way forward on general part of NR BS demodulation performance, RAN4#90Bis

## Slide 3: Test applicability of requirements for different Rx antennas
Requirements for different Rx antennas and with low correlation level
  Define applicability rule in TS 38.141-1 section 8.1.2
    Unless otherwise stated, a BS that declares to support a set of RX antennas for a specific test case, is only required to test the defined requirements with the lowest and highest numbers of supported RX antennas, and the specific connectors used for testing are based on manufacturer declaration.
    Unless otherwise stated, the test applicability rule is applicable for all physical channels: PUSCH, PUCCH and PRACH.

## Slide 4: Test Applicability for CA
Test applicability for CA
  Define CA demodulation requirements for CP-OFDM PUSCH only
    For a BS supporting UL carrier aggregation, for the highest SCS in each FR, the CC combination with the largest aggregated bandwidth is used for the test.
    If there is more than one combination, the CC combination with the largest number of CCs is used for the test.
    Mixed SCS CA combination is not to be tested for within a frequency range, considering the test complexity
    Verify the performance per CC basis
    Note: when capture the agreement in the draft CR, it should be considered that there is no requirement defined for FR1 60kHz.
Declaration of the support of UL baseband CA
  FFS: the existing RF declarations (D.38/39/40 in 38.141-1 and D.60/1/2 in 38.141-2) can be reused

## Slide 5: FR2 OTA test with SNR > 20dB
How to handle the FR2 OTA tests with SNR > 20dB (note: the 20dB threshold is for test requirements in TS 38.141-2)
  Keep the performance requirements in TS 38.104
  For test requirements in TS 38.141-2
    Add a remark in TS 38.141-2 applicable rule stating that FR2 minimum performance requirements, which require a SNR value of >[20]dB in TS 38.141-2 , cannot reliably be tested OTA. Furthermore, capture the SNR values in the corresponding test cases as “n/a”.

## Slide 6: AWGN power level setting for FR1
For FR1 PUSCH, use the following AWGN power level for BS type 1-O
For FR1 PUCCH and PRACH, the AWGN power level is 3dB higher than that for FR1 PUSCH
Remove the square brackets on the AWGN values for both FR1 conducted and OTA in this meeting
BS type | Sub-carrier spacing (kHz) | Channel bandwidth (MHz) | AWGN power level
BS type 1-O | 15 | 5 | -86.5 - ΔOTAREFSENS dBm / 4.5MHz
 |  | 10 | -83.3 - ΔOTAREFSENS dBm / 9.36MHz
 |  | 20 | -80.2 - ΔOTAREFSENS dBm / 19.08MHz
 | 30 | 10 | -83.6 - ΔOTAREFSENS dBm / 8.64MHz
 |  | 20 | -80.4 - ΔOTAREFSENS dBm / 18.36MHz
 |  | 40 | -77.2 - ΔOTAREFSENS dBm / 38.16MHz
 |  | 100 | -73.1 - ΔOTAREFSENS dBm / 98.28MHz

## Slide 7: AWGN power level setting for FR2
1: AWGN power level at the BS input [CP-OFDM, DFT-s-OFDM PUSCH, PUCCH and PRACH]
BS type | Sub-carrier spacing (kHz) | Channel bandwidth (MHz) | AWGN power level
BS type 2-O | 60 | 50 | [EISREFSENS_50M + ΔFR2_REFSENS + 15 dBm / 47.52MHz]
 |  | 100 | [EISREFSENS_50M + 3.0 + ΔFR2_REFSENS + 15 dBm / 95.04 MHz]
 | 120 | 50 | [EISREFSENS_50M + ΔFR2_REFSENS + 15 dBm / 46.08 MHz]
 |  | 100 | [EISREFSENS_50M + 3 + ΔFR2_REFSENS + 15 dBm / 95.04 MHz]
 |  | 200 | [EISREFSENS_50M + 3 + 3.0 + ΔFR2_REFSENS + 15 dBm / 190.08 MHz]
Note 1: Refer to Table 10.3.3-1 in TS 38.104 for specific EISREFSENS_50M value for different BS type. Note 2: ΔFR2_REFSENS = -3dB as per the declaration of D.54 in Table 4.6-1. |  |  | 
2: Aim to remove the square brackets for BS type 2-O in the next meeting

## Slide 8: AWGN power level setting for OTA
Discuss whether to add some notes in the OTA AWGN power level setting table:
Option 1: Do not add any notes
Option 2: Add editor notes, such as
  ΔOTAREFSENS as declared in D.xx in table 4.6-1
  ΔFR2_REFSENS = -3dB as per the declaration of D.54 in Table 4.6-1.
  EISREFSENS_50M as declared in D.28 in table 4.6-1.

## Slide 9: Direction for BS type 1-O OTA test
Option 1: receiver target reference direction (see D.31 in table 4.6-1 (the existing one in the spec TS 38.141-2).
  Option 2: OTA REFSENS receiver target reference direction
  To be decided in the next meeting

## Slide 10: Handling of BS performance requirements
Deadline for the results submission and square bracket removal
For MU and TT for OTA test
  Remove the square brackets by October meeting this year (RAN4#92bis).
For test cases agreed before the RAN4#90 meeting:
  Set deadline for simulation results submission for Rel-15 minimum requirements to October meeting this year (RAN4#92bis). No more results will be accepted unless technical issues with the requirements setup are identified.
  Remove the square bracket for performance requirements at November meeting (RAN4#93)
For the remaining test cases agreed after the RAN4#90 meeting, i.e.,
  Multi-slot PUCCH
  HST PUSCH, HST PRACH
  UCI multiplexing on PUSCH
  Aim to stabilise and align the simulation results until RAN4#92 (August). Set deadline for simulation result submission for RAN4#93 (November) and aim to also remove square brackets at RAN4#93 (November).
Deadline for updating the results in this meeting: Wednesday evening

## Slide 11: Terminology for test parameters
Companies are encouraged to check if the terminology for PUCCH and PRACH test parameters are aligned with core specifications in the next meeting