## Slide 1: WF on performance requirements of UCI Multiplexing on PUSCH
R4-1907240
Document for: Approval
3GPP TSG-RAN WG4 RAN#91
Reno, US, 13th– 17th May, 2019
Agenda: 6.12.2.2.1
Samsung, […]

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15, RAN4#87
  R4-1809366, WF on NR PUSCH demodulation requirements, RAN4#AH1807
  R4-1811694, WF on NR PUSCH demodulation requirements, RAN4#88
  R4-1813942, WF on NR PUSCH demodulation requirements, RAN4#88bis
  R4-1816347, WF on NR PUSCH demodulation requirements, RAN4#89
  R4-1902439, WF on Performance requirement of UCI Multiplexing on PUSCH, RAN4#90
  R4-1904716, WF on Performance requirement of UCI Multiplexing on PUSCH, RAN4#91

## Slide 3: DMRS configuration
FR2 DMRS configuration
  Option 1: add test case of DMRS configuration with 1+1 for FR2 with MCS 16, and agree on the corresponding CRs in the next meeting

## Slide 4: PTRS configuration
With PTRS configuration
  Frequency density (KPT-RS)=2
  Time density (LPT-RS)=1
Add test case of without PTRS configuration for FR2 with MCS 16, and agree on the corresponding CRs in the next meeting

## Slide 5: Test Applicability
Time domain allocation scheme
  Both Type A and Type B with slot-based time domain allocation was specified for requirement of UCI over on PUSCH in FR1
  The requirements for Type A and Type B are only applicable according to BS declaration
  The test applicability with Type A and Type B of UCI over on PUSCH are same as PUSCH resource mapping Type A and Type B

## Slide 6: UCI parameters
Number of payload:
  7 bits(CSI part1=5bits, CSI part2=2bits)
  40 bits(CSI part1= 20bits, CSI part2 =20bits)
Payload content:
  7 bits:
    [c0 c 1 c2 c3 c4]=[0 1 0 1 0] for CSI part1, c0 is mapped to RI information bits
    [c0 c1]=[1 0] for CSI part2 information bit
  40 bits: Select random payload content for CSI part1 and part2 in the (20,20) configuration

## Slide 7: Simulation Assumptions, UCI over PUSCH
Parameter |  | Value | 
 |  | FR1 | FR2
General System | Transform precoding | Disabled | Disabled
 | Number of Tx | 1 | 1
 | Number of Rx | 2 | 2
 | Number of layers | 1 | 1
 | [Uplink-downlink allocation for TDD] | 30 kHz SCS: 7D1S2U, S=6D:4G:4U | 120kHz SCS: 3D1S1U, S=10D:2G:2U
 | Code block group based PUSCH transmission | Disabled | Disabled
 | MCS index | 16 | 16
 | Propagation Condition | MCS 16: TDL-C 300ns, 100 Hz | MCS 16: TDL-A 30ns, 300Hz
HARQ | Maximum number of HARQ transmission | 1 | 1
 | RV | 0 | 0
DMRS | DMRS configuration type | 1 | 1
 | Maximum number of OFDM symbols for front loaded DMRS | 1 | 1
 | Number of additional DMRS symbols | 1 | 0, 1
 | Number of DMRS CDM group(s) without data | 2 | 2
 | EPRE ratio of PUSCH to DMRS | -3 dB | -3 dB
 | DMRS port | 0 | 0
 | DMRS sequence generation | NID=0, nSCID =0 | NID=0, nSCID =0
Time domain resource | PUSCH mapping type | A, B | B
 | PUSCH starting symbol index | 0 | 0
 | PUSCH symbol length | 14 | 10
Frequency domain resource | Carrier frequency (GHz) | 4 | 30
 | SCS and BW | 30kHz: 10 MHz | 120kHz: 50 MHz
 | RB assignment | Full applicable test bandwidth | Full applicable test bandwidth
 | Frequency hopping | Disabled | Disabled
PTRS configuration | Frequency density (KPT-RS) | no PTRS | 2 , without PTRS
 | Time density (LPT-RS) | no PTRS | 1, without PTRS
UCI | UL-SCH | With | With
 | Payload (bits) | Case 1: csi_part1= 5, csi_part2 =2 Case 2 : csi_part1=20,csi_part2=20 | Case 1: csi_part1 = 5 ,csi_part2 = 2 Case 2: csi_part1=20, csi_part2=20
 | uci-on-pusch-scaling | 1 | 1
 | I^HARQ_ACK | 11 | 11
 | I^CSI-1 and I^CSI-2 | 13 for CSI part1 and part2 | 13 for CSI part1 and part2
Test metric |  | 0.1% BLER of UCI with CSI part1, 1% BLER of UCI with CSI part2 | 0.1% BLER of UCI with CSI part1, 1% BLER of UCI with CSI part2