## Slide 1: WF on Multi-slot PUCCH
R4-1907242
Document for: Approval
3GPP TSG-RAN WG4 RAN#91
Reno,Nevada, USA, 13th – 17th May, 2019
Agenda: 6.12.2.1
ZTE, […]

## Slide 2: Background
The following WF was approved on NR multi-slot PUCCH :
  R4-1904719, WF on multi-slot PUCCH, RAN490bis
  R4-1902441, WF on multi-slot PUCCH, RAN4#90
The following contributions discussed in RAN4#90bis:
  R4-1903209 On NR PUCCH demodulation requirements, Nokia
  R4-1903279 Discussion on multi-slot NR PUCCH, ZTE
  R4-1903281 Simulation results for multi-slot PUCCH, ZTE
  R4-1903365 Remaining issues on performance requirements for NR PUCCH in Rel-15

## Slide 3: Background (Cont’d)
Open issue in the previous meeting [RAN4#90bis R4-1904719]:
Frequency hopping
  Option 1: Inter-slot frequency hopping enabled and intra-slot frequency hopping disabled
  Option 2: both intra and inter slot frequency hopping are disabled
  Option 3: Inter-slot frequency hopping disabled, and intra-slot frequency hopping enabled

## Slide 4: Frequency hopping
Frequency hopping
  Option 1: Inter-slot frequency hopping enabled and intra-slot frequency hopping disabled
  Option 2: both intra and inter slot frequency hopping are disabled
  Option 3: Inter-slot frequency hopping disabled, and intra-slot frequency hopping enabled
Agreement:
  Option 1 for multi-slot PUCCH performance requirements

## Slide 5: Simulation assumptions (summary)
Parameters |  | PUCCH Format 1
BandWidth/SCS |  | 40 MHz/ 30kHz
Antenna |  | 1T8R
Propagation condition |  | TDLC300-100;
Carrier frequency (GHz) |  | 4GHz;
(#Bits, #Symbols, #PRBs) |  | (2, 14,1)
initialCyclicShift |  | 0
StartingSymbolIndex |  | 0
Index of orthogonal sequence (time-domain-OCC) |  | 0
Inter/Intra-slot frequency hopping |  | Inter-slot frequency hopping Enabled
 |  | Intra-slot frequency hopping disabled
number of slot |  | 2
Test metric | DTX to Ack probability <1% | √
 | Missed Ack probability < 1% | √
 | NACK2ACK < 0.1% | √