## Slide 1: WF on high speed related requirements for NR BS demodulation in Rel.15
3GPP TSG-RAN WG4 Meeting #91
Reno, US, 13th – 17th May 2019
Agenda item: 6.12.2.1.2 [NR_newRAT-Perf]
Document for: Approval
R4-1907243
NTT DOCOMO, INC.

## Slide 2: Background
In RAN #81, it was approved to discuss HST in TEI15 after December 2018 [1].
The UE and BS demodulation performance requirements under HST scenarios are treated in TEI15 after December 2018.
In RAN #82, performance requirements for high speed train was captured as one of the remaining open issues in SR [2].
In RAN4 #90, WF was approved [3].
In RAN4 #90bis, WF was approved [4].
In RAN4 #91, NR BS performance requirements for high speed were discussed based on contributions [5-14].

## Slide 3: Way forward
  For NR BS HST requirements
  In this meeting, target to endorse the framework draft CRs with the parameters and requirement values as TBD.
  Rel-15 requirement will be only defined for scenarios where the feasibility is confirmed
  If some Rel-15 requirements are to be defined, the applicability of these requirements is based on BS declaration.

## Slide 4: HST parameters
Maximum Doppler shift
  30 kHz SCS:
    2000Hz (300km/h@Band n77(3.6GHz))
  15 kHz SCS:
    1340Hz (350km/h@Band n1(2.1GHz)) if there is no technical issue identified
    1150Hz (300km/h@Band n1(2.1GHz)) if there is some technical issue with 1340Hz
    Decision to be made in the next meeting based on the evaluation.

## Slide 5: Test parameters: PUSCH for HST
Antenna configuration
  1x2
MCS index
  MCS 2
SCS and bandwidth
  CP-OFDM
    15kHz: 5MHz, 20MHz
    30kHz: 10MHz, 100MHz
  DFT-S-OFDM
    15kHz: 5MHz
    30kHz: 10MHz
Testing metric
  SNR @70% of maximum throughput

## Slide 6: Test parameters: PUSCH for HST
DMRS configuration for both 15 kHz SCS and 30 kHz SCS
  DMRS 1+1+1
PUSCH mapping type
  type A
l0 for PUSCH mapping type A
  Option 1: l0 = 3
  Option 2: l0 = 2
  If it is not possible to make decision in this meeting, pick one test case for performance comparison in the next meeting.
Waveform
  DFT-S-OFDM and CP-OFDM
PRB allocation for DFT-s-OFDM
  The same configuration as the existing DFT-s-OFDM PUSCH test
PTRS
  without PTRS

## Slide 7: Test parameters: PUSCH for HST
Parameter | value | 
 | FR1 | FR1
Transform precoding | Disabled | Enabled
Number of Tx | 1 | 1
Number of Rx | 2 | 2
Number of layers | 1 | 1
DMRS type | type 1 | type 1
Number of DMRS symbols | DMRS 1+1+1, Front loaded DMRS start symbol Option 1: lo= 3 Option 2: lo= 2 | DMRS 1+1+1, Front loaded DMRS start symbol Option 1: lo= 3 Option 2: lo= 2
symbols length | 14 | 14
start symbol index | 0 | 0
Time domain resource allocation type | type A | type A
Frequency domain resource | Full applicable test bandwidth | 15kHz: 25 PRB; 30kHz: 24 PRB (middle of test BW)
MCS index | 2 | 2
Carrier frequency (GHz) | 15kHz SCS: 2.1GHz 30kHz SCS: 3.6GHz | 15kHz SCS: 2.1GHz 30kHz SCS: 3.6GHz
Propagation condition | Scenario 3 with AWGN in the next slide | Scenario 3 with AWGN in the next slide
SCS and BW | 15kHz: 5MHz, 20MHz 30kHz: 10MHz,, 100MHz | 15kHz: 5MHz; 30kHz: 10MHz
PTRS | Without | Without
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput

## Slide 8: Test parameters: PUSCH for HST
HST Scenario
Parameter | Value
 | Scenario 3
 | 300 m
 | 2 m
 | 300 km/h for fd=1150Hz, 2000Hz FFS: 350 km/h for fd=1340Hz
 | For 15kHz SCS: - 1340Hz (350km/h@Band n1(2.1GHz)) if there is no technical issue identified - 1150Hz (300km/h@Band n1(2.1GHz)) if there is some technical issue with 1340Hz - Decision to be made in the next meeting based on the evaluation. For 30kHz SCS: - 2000Hz (300km/h@Band n77(3.6GHz))

## Slide 9: Test parameters: PRACH for HST
Frequency offset under AWGN
  Frequency offset for restricted set Type B
    Option 1: 1875 Hz
    Option 2: 625 Hz, 2000 Hz (DCM)
  Frequency offset for restricted set Type A
    Option 1: 1340Hz
    Option 2: 625Hz, 1340Hz
    Other options are not precluded
Frequency offset under fading
  Frequency offset for restricted set Type A and B
    Option 1: TDLC300-100 with FO 400 Hz (Baseline in RAN4#90Bis meeting)
    Option 2: TDLC300-a with FO 400 Hz, where a= {1340, 1875, 2000}Hz
HST PRACH requirement tests shall apply only for the restricted set type declared to be supported. If both type A and type B are declared to be supported, the tests shall be done for either type A or type B.

## Slide 10: Test parameters: PRACH for HST
The PRACH requirements will be defined with the following antenna configuration:
  Tx: 1 antenna
  Rx: 2, 4, and 8 antennas
The applicability rule will be specified to down-select the test cases to be run for a BS.
  Follow the general applicability rule for BS
Test metric (Same as other PRACH tests)
  False alarm probability: 0.1%
  missed detection: 99%

## Slide 11: Test parameters: PRACH for HST
Test preamble configuration (Ncs, logical sequence index, v)
Burst format | Restricted Set | Ncs | Logical sequence index | v
0 | Type A | 15 | 384 | 0
 | Type B | 15 | 30 | 30

## Slide 12: Reference
[1] RP-182149, “Way forward on RAN4 work for Core and Perf. part for NR”, RAN4 Chairman, RAN #81
[2] RP-182805, “Status Report of WI on New Radio Access Technology”, NTT DOCOMO,INC., RAN #82
[3] R4-1902442, “WF on high speed related requirements for NR BS demodulation in Rel.15”, NTT DOCOMO, INC., RAN4#90
[4] R4-1904720, “WF on high speed related requirements for NR BS demodulation in Rel.15”, NTT DOCOMO, INC., RAN4#90bis
[5] R4-1905430, “Discussion and simulation results for NR HST PUSCH”, Samsung, RAN4#91
[6] R4-1905434, “Discussion and simulation results for NR HST PRACH”, Samsung , RAN4#91
[7] R4-1905660, “Discuss on HST demodulation requirements for Rel-15 NR BS”, Huawei, RAN4#91
[8] R4-1906368, “NR Rel-15 HST evaluation results”, Nokia, RAN4#91
[9] R4-1905997, “HST for NR BS demod in Rel-15 - PUSCH considerations”, Ericsson, RAN4#91
[10] R4-1905998, “HST for NR BS demod in Rel-15 - PRACH considerations”, Ericsson, RAN4#91
[11] R4-1906372, “On high speed train related PUSCH requirements for NR BS demodulation in Rel-15”, Nokia, RAN4#91
[12] R4-1906373, “On high speed train related PRACH requirements for NR BS demodulation in Rel-15”, Nokia, RAN4#91
[13] R4-1906995, “NR PUSCH for high speed in Rel.15”, NTT DOCOMO, INC., RAN4#91
[14] R4-1907157, “NR PRACH for high speed in Rel.15”, NTT DOCOMO, INC., RAN4#91