## Slide 1: WF on CLI measurement
3GPP TSG-RAN WG4 Meeting #91 Reno, US, 13 - 17 May 2019
Agenda Item: 8.2.3
R4-1907385
LG Electronics

## Slide 2: Background
Based on the WF (R4-1904763) in last RAN4 meeting,
  RAN4 needs to clarify remaining issue for SRS-RSRP and CLI-RSSI measurement.
  RAN4 should start evaluation for SRS-RSRP measurement accuracy requirement.

## Slide 3: SRS-RSRP measurement
SRS-RSRP measurements resource configuration
  Based on R4-1904763, the parameters for SRS-RSRP measurement resource configuration is finalized as following table, and RAN4 needs to send LS to RAN2
Parameter name in specification | Final decision in RAN4
SRS-scs | 15, 30, 60 kHz for FR1 60, 120 kHz for FR2
nrofSRS-Ports | 1
transmissionComb | n2 comboffset (0,1), cyclicShift (0,…,7) n4 comboffset (0,..,3), cyclicShift (0,…,11)
resourceMapping | startPosition INTEGER (0,…,5) nrofSymbols ENUMERATED {n1} repetitionFactor ENUMERATED {n1}
freqDomainPosition | 0,…,67
freqDomainShift | 0,…,268
freqHopping | no
groupOrSequenceHopping | no
SRS-Measurement-PeriodicityAndOffset (only periodic) | sl1 NULL, sl2 INTEGER(0..1), sl4 INTEGER(0..3), sl5 INTEGER(0..4), sl8 INTEGER(0..7), sl10 INTEGER(0..9), sl16 INTEGER(0..15), sl20 INTEGER(0..19), sl32 INTEGER(0..31), sl40 INTEGER(0..39), sl64 INTEGER(0..63), sl80 INTEGER(0..79), sl160 INTEGER(0..159), sl320 INTEGER(0..319), sl640 INTEGER(0..639)

## Slide 4: SRS-RSRP measurement requirement
DL Measurement timing error
  Define at least timing error value as conditions for test case
    Option 1: [13.5]usec for FR1 and [7.2]usec for FR2
    Option 2: other values are not precluded for further analysis
  FFS how to capture the condition on the timing error in the accuracy requirement
    Timing error without constant offset
      E.g.) Te_CLI = (NTA_offset + NTA)A + Dpropagation_V – Dpropagtion_V2A
        (NTA_offset + NTA)A : timing advance for aggressor(A) UE
        Dpropagation_V : downlink propagation delay for victim(V) UE from the gNB of the victim UE
        Dpropagtion_V2A : propagation delay from aggressor(A) UE to victim(V) UE
  Constant offset value for timing adjustment for SRS-RSRP measurement is up to UE implementation
Cyclic shift
  Limitation on the distance between the cyclic shifts of two SRS resource on the same symbol and same comb is to be considered for the accuracy requirements
  Companies are encouraged to provide evaluation for performance impact on cyclic shift configuration
  FFS whether and how to capture the condition of cyclic shift in the accuracy requirement

## Slide 5: SRS-RSRP measurement requirement
Side condition
  Option 1: SINR -3dB
  Option 2: SINR -1dB
  Other options are not precluded
The number of RB for SRS resource
  Option 1: 48 RBs
  Option 2: 24 RBs
  Other options are not precluded
The number of sample for measurement accuracy
  Option 1: 3 samples
  Option 2: 5 samples
  Other options are not precluded
The dependency of measurement accuracy
  RAN4 needs further discussion how to define measurement accuracy

## Slide 6: UE behavior for CLI measurement
QCL assumption
  For FR2 CLI measurement, a UE uses the same spatial filter of UE Rx beams as used one of the latest received PDSCH and the latest monitored CORESET.
  send LS to RAN1 for the QCL assumption agreement

## Slide 7: UE behavior for CLI measurement
Scheduling restriction for CLI measurement
  SRS-RSRP measurement
    Depending on the UE capability, UE is not expected to receive PDCCH/PDSCH on SRS-RSRP measured OFDM symbols, and on Y data symbol before SRS-RSRP measured symbol in intra-band CA.
      Y depends on SCS (e.g., Y = 1 or 2) and detail value will be defined in next meeting.
  CLI-RSSI measurement
    Depending on the UE capability, UE is not expected to receive PDCCH/PDSCH on CLI-RSSI measured OFDM symbols in intra-band CA.
      FFS for scheduling restriction on X data symbol before CLI-RSSI measured symbol
  RAN4 needs to send LS to RAN1 to clarify the UE capability for FDMed between PDSCH and CLI measurement resources.

## Slide 8: CLI measurement reporting
Measurement reporting range
  Include ‘too strong signal to measure’ as one of the possible reported value
    FFS to reuse “infinity” in L3-RSRP reporting range in TS38.133 for SRS-RSRP and add similar contents for RSSI reporting range