## Slide 1: Way forward on FR2 RRM RMC for 2AoA test setup
Ericsson
3GPP TSG-RAN WG4 Meeting #91
Reno, NV, USA, 13 – 17 May, 2019
R4-1907389

## Slide 2: Background
For two AoA tests, use TDM transmissions between the two angles in Rel-15.
  Add a scheduling parameter to the RMC’s to specify in which slot each AoA can transmit/receive.
  OCNG, TCI and Tx beam (SSB and CSI-RS) will be considered

## Slide 3: Agreements of TDM’ed OCNG/RMC/SSB/CSI-RS patterns for test setup #3
OCNG is not transmitted on the symbols where SSB/CSI-RS is transmitted in the same probe
Only SSB/CSI-RS is transmitted from the probe not transmitting the serving beam
When serving probe is transmitting then there is no signal on the non-serving probe and vice versa
FFS how to ensure Io doesn’t vary much with time in the test.
  Option 1: Align the RMC/OCNG transmission bandwidth with SSB and/or CSI-RS band