## Slide 1: WF on NSA FDD-TDD HPUE CHTTL, China Unicom, …
3GPP TSG-RAN WG4 Meeting #91 R4-1907453 Reno, USA, 13th May – 17th May, 2019

## Slide 2: Backgrounds
The scope of PC2 FDD-TDD including the following two cases:
  Note: for case 1 and case 2, the duty cycles of NR TDD can be different.
  RAN4 study starts from case 1, but case 2 is not precluded.
  Example band combination for this study is DC_3_n78
Wayforwards R4-1902452, R4-1905004 are agreed in RAN4#90, 90bis respectively
 | EN-DC total power | LTE maximum power | NR maximum power
Case 1 | 26dBm | 23dBm | 23dBm
Case 2 | 26dBm | 23dBm | 26dBm
Background from WF R4-1902452:
Further study the following solutions to meet the overall uplink duty cycle for the PC2 FDD-TDD HPUE, starting from case 1
  Option 1: Reduce Tx time for LTE FDD UL
    Restrict LTE FDD UL transmission by TDM patterns can be considered as the starting point for option 1
  Option 2: Reduce Tx power for LTE FDD UL
  Other options are not precluded

## Slide 3: Wayforward for PC2 FDD-TDD HPUE
Wayforward for RAN4#91:
For case 1 PC2 FDD-TDD HPUE
  One capability per band combination is considered to reflect the overall maximum UL duty cycle up to 100% for the PC2 FDD-TDD HPUE
    Default value should be 50%
  Further discuss the relationship between the duty cycle for LTE and NR, max LTE and NR power, and the UE capability to reflect the overall maximum UL duty cycle in the next meeting, starting from the following equation:
    PLTE, PNR, P26 represent the maximum linear power (mW) of LTE, NR, and EN-DC power class 2 respectively; DutyLTE, DutyNR, DutyEN represent the normalized uplink duty cycle of LTE, NR and EN-DC respectively. MaxUplinkDutyCycle represents the overall maximum UL duty cycle may be able to maintain the PC2 power subject to P-MPR
  Note that this equation is aligned with the majority view in this meeting
Companies are encouraged to provide solutions in the next meeting taking above into account
DutyEN = DutyLTE * ( PLTE/ P26) + DutyNR *(PNR/ P26), DutyEN ≤ MaxUplinkDutyCycle ….(1)

## Slide 4: Reference
  [1] R4-1905555 Further discussion on NSA FDD-TDD HPUE SAR solutions OPPO
  [2] R4-1906286 EN-DC power for FDD-TDD PC2 Ericsson
  [3] R4-1906469 Further discussion on solutions for EN-DC FDD-TDD High Power UE CHTTL
  [4] R4-1906858 On SAR solutions for FDD+TDD HPUE Huawei, HiSilicon
  [5] R4-1906859 On deriving FDD+TDD TDM pattern based on max UL duty cycle capability Huawei, HiSilicon
  [6] R4-1907118 SAR mitigation for PC2 FDD-TDD EN-DC Qualcomm Incorporated