## Slide 1: WF on NSA FDD-TDD HPUE CHTTL, China Unicom, OPPO
3GPP TSG-RAN WG4 Meeting #91 R4-1907488 Reno, USA, 13th May – 17th May, 2019

## Slide 2: Backgrounds
The scope of PC2 FDD-TDD including the following two cases:
  RAN4 study starts from case 1, but case 2 is not precluded.
  Example band combination for this study is DC_3_n78
Way forwards R4-1902452, R4-1905004 are agreed in RAN4#90, 90bis respectively
 | EN-DC total power | LTE maximum power | NR maximum power
Case 1 | 26dBm | 23dBm | 23dBm
Case 2 | 26dBm | 23dBm | 26dBm
Background from WF R4-1902452:
Further study the following solutions to meet the overall uplink duty cycle for the PC2 FDD-TDD HPUE, starting from case 1
  Option 1: Reduce Tx time for LTE FDD UL
    Restrict LTE FDD UL transmission by TDM patterns can be considered as the starting point for option 1
  Option 2: Reduce Tx power for LTE FDD UL
  Other options are not precluded

## Slide 3: Wayforward for PC2 FDD-TDD HPUE
For case 1 PC2 FDD-TDD HPUE
  Further discuss
    The relationship between the duty cycle for LTE and NR, max LTE and NR power, and the maximum UL duty cycle for PC2 FDD-TDD EN-DC in the next meeting, starting from the following equation:
    PLTE, PNR, P26 represent the maximum linear power (mW) of LTE, NR, and EN-DC power class 2 respectively; DutyLTE, DutyNR represent the normalized uplink duty cycle of LTE and NR respectively.
    Duty threshold is the maximum UL duty cycle used to maintain the PC2 power class for FDD+TDD ENDC HPUE.
    The SAR effect differences for FDD and TDD bands will be considered.
    How to reflect the SAR difference for different bands in the above equation will be further studied.
    P-MPR can always be used by UE for SAR when necessary.
  Other solutions are not precluded.
DutyLTE*(PLTE/ P26) + DutyNR*(PNR/ P26) ≤ Duty threshold….(1)

## Slide 4: Reference
  [1] R4-1905555 Further discussion on NSA FDD-TDD HPUE SAR solutions OPPO
  [2] R4-1906286 EN-DC power for FDD-TDD PC2 Ericsson
  [3] R4-1906469 Further discussion on solutions for EN-DC FDD-TDD High Power UE CHTTL
  [4] R4-1906858 On SAR solutions for FDD+TDD HPUE Huawei, HiSilicon
  [5] R4-1906859 On deriving FDD+TDD TDM pattern based on max UL duty cycle capability Huawei, HiSilicon
  [6] R4-1907118 SAR mitigation for PC2 FDD-TDD EN-DC Qualcomm Incorporated