## Slide 1: WF on summary and recommendations for co-existence evaluation of CLI
LGE, Huawei, Ericsson, Nokia, Qualcomm
3GPP TSG-RAN WG4 Meeting RAN4#91 R4-1907606
Reno, USA, 13th – 17th May, 2019
Agenda: 8.2.1
Document for Approval

## Slide 2: Background
In [1], the work plan of Cross Link Interference (CLI) and Remote Interference Management (RIM) was agreed as follows:
  Objectives for CLI and RIM
    Perform coexistence study to identify conditions of coexistence among different operators in adjacent channels
      Target no or very minimal impact on RF requirement
  Time schedule for CLI
    We propose the work plan for RF aspects as follows:
      1) RAN4#90
      Identify and discuss co-existence study of CLI
        Agree on possible deployment scenarios for CLI if needed
      Approve the work plan and TR skeleton for CLI
      2) RAN4#90BIS
      Collect simulation results for CLI if needed
      Draft an initial conclusion for CLI
      3) RAN4#91
      Finalize RF co-existence study of CLI
RAN4 should finalize co-existence study in RAN4#91 based on the agreed work plan.

## Slide 3: Summary for FR1 co-existence evaluation of CLI
For the evaluated adjacent channel for FR1 scenarios, the following observations have been made for Cross link interference (CLI) based on different traffic conditions (full buffer and low traffic mode) and different BS Tx power levels without any RF requirement change or interference mitigation:
  Macro-to-Macro
      For BS to BS interference, performance degradation was observed in adjacent channel.
      No performance degradation relating to ACLR/ACS due to UE to UE interference was observed in adjacent channel.
  Indoor-to-Macro
      For BS to BS interference and UE to UE interference, no performance degradation relating to ACLR/ACS was observed in adjacent channel.
  Indoor-to-Indoor
      For BS to BS interference, no performance degradation was observed in adjacent channel based on both full buffer and low traffic mode provided that the BS and UE have similar power.
      When higher BS transmission power is assumed, some performance degradation was observed for BS to BS interference.
      For UE to UE interference, no performance degradation relating to ACLR/ACS was observed in adjacent channel based on both full buffer and low traffic mode.
  Macro-to-Indoor
      For BS to BS interference, no performance degradation was observed in adjacent channel.
      For UE to UE interference, performance degradation was observed in adjacent channel by some companies.
It is noted that there may be a possibility of UE blocking occurring but this was not investigated as the studies in this WI are focused on ACLR/ACS co-existence impact.

## Slide 4: Summary for FR2 co-existence evaluation of CLI
For the evaluated adjacent channel for FR2 scenarios, the following observations have been made for Cross link interference (CLI) based on different traffic conditions (full buffer and low traffic mode) and different BS Tx power levels without any RF requirement change or interference mitigation:
  Macro-to-Macro
      For BS to BS interference, some performance degradation was observed in adjacent channel with 100% grid shift. The extent of the observed degradation varied from minor to significant between companies. The degradations increase with lower grid shift and decrease with lower output power. For UE to UE interference, no performance degradation relating to ACLR/ACS was observed in adjacent channel.
  Indoor-to-Macro
      For BS to BS interference and UE to UE interference, no performance degradation was observed in adjacent channel.
  Indoor-to-Indoor
      For BS to BS interference, some results showed no performance degradation in the adjacent channel, and other results showed performance degradation. The performance degradation has some dependency on how power control is operated.
      For UE to UE interference, no performance degradation relating to ACLR/ACS was observed in adjacent channel based on both full buffer and low traffic mode.
  Micro-to-Micro
      Simulations were performed by 3 companies the results for BS-BS interference were contradictory as summarized below:
        no performance degradation relating to ACLR/ACS was observed
        Significant BS to BS interference was observed relating to ACLR/ACS observed
      All results showed that there was no UE to UE interference relating to ACLR/ACS.
      Some deployments in which the micro is close to the victim may cause losses in a victim network, but this is lost in the statistics. Operators may need to take care about the distance between micros in close range.
  It is noted that there may be a possibility of UE blocking occurring but this was not investigated as the studies in this WI are focused on ACLR/ACS co-existence impact.

## Slide 5: Recommendations for co-existence evaluation of CLI
<FR1>
  Macro-to-Macro
    Performance degradation was observed from the BS-to-BS interference for macro-macro scenario, which suggests that dynamic TDD should not be operated in such scenarios.
  Indoor scenarios (Indoor-to-Macro & Indoor-to-Indoor)
    Performance degradations were not observed from operating dynamic TDD between an indoor network and a macro network and vice versa if there is sufficient isolation between them. No significant impact from operating dynamic TDD for the indoor scenario was observed as long as the BS and UE powers are similar and the operators co-ordinate so that basestation positions are offset. If higher BS power is assumed, some throughput degradation in the indoor scenario was observed due to BS to BS interference. The observations imply that dynamic TDD can be used in indoors as long as care is taken.

## Slide 6: Recommendations for co-existence evaluation of CLI
  <FR2>
  Macro-to-Macro
  Some performance degradation was observed from the BS-to-BS interference for macro-macro scenario. The differences in the simulation results imply that operating dynamic TDD in this scenario without impact to neighbor network may be deployment dependent and requires at least careful planning and collaboration between operators to avoid performance impact.
Indoor scenarios (Indoor-to-Macro & Indoor-to-Indoor)
  Performance degradations were not observed from operating dynamic TDD between an indoor network and a macro network if there is sufficient isolation between them. Results suggested that to avoid degradation, careful layout and parameterization are necessary for indoor to indoor scenario. Overall, the observations imply that dynamic TDD can be used indoors as long as care is taken.
Micro-to-micro
  For micro to micro, the differences in the simulation results imply that to avoid BS to BS interference, operators may need to consider the proximity of micro BS in the same area. Overall, the observations imply that dynamic TDD can be used in certain micro deployments as long as care is taken.

## Slide 7: References
[1] R4-1905522, “[CLI] Discussion on CLI co-existence simulation results for FR1” , Huawei, HiSilicon
[2] R4-1905523, “[CLI] Discussion on CLI co-existence simulation results for FR2” , Huawei, HiSilicon
[3] R4-1906045, “ Co-existence simulation results of CLI for FR1” , LGE
[4] R4-1906046, “ Co-existence simulation results of CLI for FR2” , LGE
[5] R4-1906097, “Simulation results for urban macro 4GHz” , Ericsson
[6] R4-1906098, “Simulation results for urban macro 30GHz” , Ericsson
[7] R4-1906099, “Simulation results for indoors 4GHz” , Ericsson
[8] R4-1906100, “Simulation results for indoors 30GHz” , Ericsson
[9] R4-1906101, “Simulation results for micro 30GHz” , Ericsson
[10] R4-1906703, “ Qualcomm results for UE-to-UE CLI” , Qualcomm
[11] R4-1906879, “TP to TR 38.828 ACI simulation results” , Nokia