## Slide 1: WF on switching and interruption time for MIMO layer adaption for power saving
CATT, Huawei, Huawei Device, vivo
3GPP TSG-RAN WG4 Meeting #91 R4-1907615
Reno, USA, 13th – 17th May 2019

## Slide 2: Background
The objective of the UE power saving includes the following [1] item that needs RAN4 study.
Evaluate the required switching and interruption times for UE dynamic adaptation to the maximum number of MIMO layers [RAN4]
In RAN4#91 meeting, several contributions [2-5] were received regarding the RAN4 scope in the WID. During the discussions, it was proposed to use the BWP switching requirement frame work as the starting point for further study and the following cases need to be studied for MIMO layer adaption.
  Case 1: MIMO layer adaption without BWP change
  Case 2: MIMO layer adaption with BWP change

## Slide 3: Switching time for MIMO layer adaption
To ensure power saving gain of MIMO layer adaption, it is anticipated that UE shall have the ability to switch ON/OFF its transmitter/receiver and apply the new MIMO layer configurations within a specific time delay.
The MIMO layer adaption delay could be tentatively defined as [the time duration from end of the control symbol carrying switching command to the start of the new MIMO layer configurations in slot n+Y].
3 time components are considered to be relevant for MIMO layer adaption, e.g.
The time required for PDCCH decoding time
New parameter calculating and loading
Applying the new parameters
Final delay (y) to be specified
PDCCH symbols
MIMO layer switching CC
time
DCI parsing
New parameters calculating and loading
Applying the new parameters
Start of slot n+y for new MIMO layer configuration
Start of slot n carrying DCI switching command
Potential interruption
MIMO layer switch delay

## Slide 4: Interruption time
During the process of MIMO layer adaption, the ON/OFF switch of UE RF chain may cause potential interruption to the ongoing communications on active RF chains.

## Slide 5: Way forward
Companies are encouraged to analyze on the time components for MIMO layer adaption delay.
  Inputs from chipset vendors are highly anticipated.
Study whether interruption time need to be specified for communications on active RF chains due to MIMO layer adaption.
Confirm whether BWP switching requirement frame work can be reused.
Study how to capture the requirements for MIMO layer adaption in the specifications.

## Slide 6: Reference
[1] RP-190727, New WID: UE Power Saving in NR, CATT
[2] R4-1905381, Discussion on RF aspects related to dynamic adaption for power saving, CATT
[3] R4-1905530, Evaluation of switching and interruption time for UE antenna switching, vivo
[4] R4-1905879, UE RF tuning time for MIMO layer switching, Ericsson
[5] R4-1906660, Discussion on UE dynamic adaptation to the maximum number of MIMO layers, MediaTek inc.