## Slide 1: WF on the R16 IAB scope
Ericsson,
3GPP TSG-RAN4 Meeting #91 R4-1907617
Reno, USA, 13-17 May, 2019

## Slide 2: Background
IAB WID[1] specifies as below:
  Specification of mechanisms for resource multiplexing among backhaul and access links. This includes:
    Specification of semi-static configuration for IAB-node/IAB-donor DU resources in case of TDM operation subject to half-duplex constraint. This shall be forward compatible to allow the support of half-duplex scenarios with FDM and SDM resource sharing among backhaul and access links.
Q1: Whether FDM and SDM is in R16 scope need to be clarified

## Slide 3: Background
There is two scenarios [2] summarized in RAN4#90bis and it is current understanding that scenario 1 is TDM operation between IAB-DU,
Q2: how to interpret scenario 2 need further clarified in relation of R16 scope discussion.

## Slide 4: R16 scope clarification and discussion- Q1
The interpretation of below wording in Spec
    Physical layer specification [RAN1-led, RAN2, RAN3, RAN4]:
      Specification of semi-static configuration for IAB-node/IAB-donor DU resources in case of TDM operation subject to half-duplex constraint. This shall be forward compatible to allow the support of half-duplex scenarios with FDM and SDM resource sharing among backhaul and access links.
  FDM and SDM is not in scope of R16 for physical layer specification, but forward compatibility is required.
    the forward compatibilty requires the R16 IAB physical layer spec would not need to change due to introduction of the FDM/SDM feature in R17
  Forward compatilbity of FDM/SDM implication on RAN4 RF spec need clarified
    Possible RF requirement for Hardware design need to consider the FDM/SDM impact already in R16 to ensure the forward compatiblity (no R16 Hardware need to redesigned, only performance test will be added later)

## Slide 5: R16 scope clarification and discussion- Q2
  Half duplex contraint:
    in legacy TDD system, half duplex means the Transmitting and receiving cannot operating at the same time for the same frequency.
    Transmiting in IAB node context means:
      IAB-MT transmitting: MT:Tx
      IAB-DU transmitting: DU: Tx
    Receiving in IAB node context means:
      IAB-MT receiving: MT:Rx
      IAB-DU receiving: DU: Rx
    The half-duplex limitation in IAB node means the below combination at the same time is not possible, A: Tx and B: RX, the detail forbidden combination is listed below:
      MT: Tx and DU: Rx
      MT: RX and DU: Tx
      MT: TX and MT: Rx (traditional TDD half –duplex limitation)
      DU:TX and DU: RX (traditional TDD half –duplex limitation)

## Slide 6: R16 scope clarification and discussion- Q2
TDD pattern |  | DL | DL | DL | UL | UL
Sceanario1 | MT | MT: NULL | MT:RX | MT: NULL | MT:TX | MT: NULL
 | DU | DU:TX | DU: NULL | DU:TX | DU: NULL | DU:RX
sceanario 2 | MT | MT:TX | MT:RX | MT: NULL | MT:NULL | MT:NULL
 | DU | DU:TX | DU: NULL | DU:TX | DU:RX | DU:RX
Table 1: IAB-MT and IAB-DU in IAB-Node mapped to TDD pattern
  Scenario 1 in Table 1 fullfill the half-duplex contraint as no forbidden combiniation is used.
  Scenario 2 is Table fullfill the half-duplex contraint as no forbidden combination is used.

## Slide 7: R16 scope clarification and discussion-Q2
In TR 38.874 section 7.3.2, below text is excerpted for discussion
  In case of transmitter-side SDM/FDM, an IAB-node simultaneously transmits in the DL (to an access UE and/or child IAB-node) and transmits in the UL (to a parent IAB-node). In case of receiver-side SDM/FDM, an IAB-node simultaneous receives in the DL (from a parent node) and receives in the UL (from an access UE and/or child IAB-node).
Observation 1: (DU: TX and MT: TX) combination is SDM operation within one IAB Node

## Slide 8: R16 scope clarification and discussion-Q2
SDM operation defintion:
  Simutaneous transmission to IAB parent and IAB child still subject to the half-duplex contraint
Table 7.3.3-2: DU and MT behaviour in case of SDM operation
DL/UL/F heading of columns indicates MT configuration
 | DL | UL | F
DL-H | DU: Tx MT: NULL | DU: Tx MT: Tx | DU: Tx MT: Tx
DL-S | When DU resource: IA DU: Tx MT: NULL When DU resource: INA DU: NULL MT: Rx | When DU resource: IA DU: Tx MT: Tx When DU resource: INA DU: NULL MT: Tx | When DU resource: IA DU: Tx MT: Tx When DU resource: INA DU: NULL MT: Tx/Rx
UL-H | DU: Rx MT: Rx | DU: Rx MT: NULL | DU: Rx MT: Rx

## Slide 9: R16 scope clarification and discussion- Short summary Q1
Q1: Whether FDM and SDM is in R16 scope need to be clarified
Answer:
  FDM and SDM is not in scope of R16 for physical layer specification, but forward compatibility is required.
    the forward compatibilty requires the R16 IAB physical layer spec would not need to change due to introduction of the FDM/SDM feature in R17
  Forward compatilbity of FDM/SDM implication on RAN4 RF spec need clarified
    Possible RF requirement for Hardware design need to consider the FDM/SDM impact already in R16 to ensure the forward compatiblity (no R16 Hardware need to redesigned, only performance test will be added later)

## Slide 10: R16 scope clarification and discussion- Short summary Q2
Q2: how to interpret scenario 2 need further clarified in relation of R16 scope discussion.
Answer:
  Scenario 2 is SDM operation for single IAB node which simultaneous transmission on both IAB parent and IAB child

## Slide 11: R16 scope clarification and discussion- propsoal
Scenario 2 bring at least the following benefits:
  No regulation issue is foreseen
  IAB-MT power is the same with IAB-DU power
Scenario 2 as SDM operation need to be forward compatilbe in current WID, RAN4 need further investigate the implication of it
  Proposal: RAN4 need further clarify the implication of the forward compatility of the FDM/SDM operation.

## Slide 12: Ref
[1] RP-182882, Integrated access and backhaul for NR
[2] R4-1905105, Summary of the IAB scenario, Ericsson