## Slide 1
Samsung
WF on defining synchronized operation in BS specifications
R4-1907646

## Slide 2: Background
In TS36.104 and TS36.101 there are below definitions
  Synchronized operation: operation of TDD in two different systems, where no simultaneous uplink and downlink occur.
  Unsynchronized operation: operation of TDD in two different systems, where the conditions for synchronized operation are not met.
Furthermore, in TS36.104 sub-clause 4.5, it is mentioned that:
  For a BS capable of multi-band operation supporting bands for TDD, the RF requirements in the present specification assume synchronized operation, where no simultaneous uplink and downlink occur between the supported operating bands.
However, in TS37.105 there is no definition on synchronized and unsynchronized, but with the clarification on BS capable of multiple-band operation
  For multi-band TAB connectors and multi-band RIBs supporting the bands for TDD, the RF requirements in the present specification assume no simultaneous uplink and downlink occur between the bands.
In TS38.104 there is no definition on synchronized and unsynchronized, but with the clarification on BS capable of multiple-band operation
  For multi-band connectors and multi-band RIBs supporting the bands for TDD, the RF requirements in the present specification assume no simultaneous uplink and downlink occur between the bands.

## Slide 3: Issues in TS37.105
In sub-clause 9.7.5.2.4.2 Unsynchronized operation for BC3 defined for Unwanted emission
Co-location blocking in Table 7.5.2.2-1
  NOTE 6: Co-located TDD base stations that are synchronized and using the same or adjacent operating band can receive without special co-location requirements. For unsynchronized base stations, special co-location requirements may apply that are not covered by the 3GPP specifications.
Spurious emission for co-location in sub-clause 9.7
  NOTE 3: Co-located TDD base stations that are synchronized and using the same or adjacent operating band can transmit without special co-locations requirements. For unsynchronized base stations, special co-location requirements may apply that are not covered by the 3GPP specifications.
Spurious emission for co-existence in sub-clause 9.7
  NOTE 4: TDD base stations deployed in the same geographical area, that are synchronized and use the same or adjacent operating bands can transmit without additional co-existence requirements. For unsynchronized base stations (except in Band 46, or in Band 49), special co-existence requirements may apply that are not covered by the 3GPP specifications.
  Issue identified:
There is requirement clearly defined for “unsynchronized operation” without corresponding definition in TS37.105
Here in all the notes mentioned “synchronized” or “unsynchronized base stations” is between/among BSs rather than within one BS
In TS37.145-1/2 there are many requirement defined for “synchronized operation” or “unsynchronized operation” without corresponding definition as well

## Slide 4: Way forward for AAS specs
Synchronized operation and Unsynchronized operation shall be needed for TS37.105
  Synchronized operation: operation of TDD in two different systems, where no simultaneous uplink and downlink occur.
  Unsynchronized operation: operation of TDD in two different systems, where the conditions for synchronized operation are not met.
The same definitions shall be incorporated in conformance testing spec of TS37.145-1 and TS37.145-2 as well

## Slide 5: Issue in TS38.104
In sub-clause 6.6.5.2.3 Additional spurious emissions requirements
  NOTE 3: TDD base stations deployed in the same geographical area, that are synchronized and use the same or adjacent operating bands can transmit without additional co-existence requirements. For unsynchronized base stations, special co-existence requirements may apply that are not covered by the 3GPP specifications.
In sub-clause 6.6.5.2.4 Co-location with other base stations
  NOTE 3: Co-located TDD base stations that are synchronized and using the same or adjacent operating band can transmit without special co-locations requirements. For unsynchronized base stations, special co-location requirements may apply that are not covered by the 3GPP specifications.
  Issue identified:
Here in all the notes mentioned “synchronized” or “unsynchronized base stations” is between/among BSs rather than within one BS without clear definition in TS 38.104
There is no “(un)synchronized operation” in TS38.104

## Slide 6: Way forward for NR BS specs
Solution for TS38.104
  Option 1: reuse LTE definition of (un)synchronized operation
  Option 2: new definition e.g. (un)synchronized base stations to be introduced for NR
  Option 3: no change to TS38.104
The same solution of core spec applies for conformance testing spec of TS38.141-1 and TS38.141-2 as well