## Slide 1: WF on nominal channel spacing
ZTE, Ericsson
3GPP TSG-RAN WG4 #91 Meeting
Reno, Nevada, USA, 13th - 17th May. 2019
R4-1907686

## Slide 2
Agreement from Chairman notes:
Nominal channel spacing is independent from SCS
Issue 1: SCS-independent nominal channel spacing

## Slide 3
Agreement:
Keep GB in the nominal channel spacing equation if
    there are some way, e.g., Ericsson’s proposal, or Huawei’s proposal, smallest SCS solution, or other possible solution, to address overlapping issue.
Issue 2: Whether or not to keep GB in
Channel spacing equation

## Slide 4
For Ericsson proposal
0 out of 169 found with overlapping issues for FR1
0 out of 16 found with overlapping issues for FR2
  u=3 always  maximum SCS
Agreement :
Keep GB in the equation to calculate nominal channel spacing
No overlapping issue
Issue 2: Whether or not to keep GB in
Channel spacing equation(Cont’d)
Notes: Showing results_EricssonProposal.txt

## Slide 5
Issue 3: SCS selection
SCS selection relates to GB and n in the equation
Option 1: use maximum u supporting both CBWs
For a combination (CBW1, CBW2), find maximum u supporting both CBW1 and CBW2  labelled as u_target
Look-up table for GB1 corresponding to (u_target, CBW1)
Look-up table for GB2 corresponding to (u_target, CBW2)
Use n = u_target in the equation
No overlapping issues
Minimized spec impact

## Slide 6
Issue 3: SCS selection (Cont’d)
Option 2: use reference SCS
For a combination (CBW1, CBW2), determine the reference SCS by
  Identifying a TBC covering all the other TBCs
  Selecting the SCS corresponding to the identified TBC as the reference SCS labelled as u_target
Look-up table for GB1 corresponding to (u_target, CBW1)
Look-up table for GB2 corresponding to (u_target, CBW2)
Use n = u_target in the equation
Not working for Scenario 1 or Scenario 3 (partially or non-overlapped)
Ambiguity in Scenario 4
Dependent on a specific configuration

## Slide 7
Issue 3: SCS selection (Cont’d)
Option 3: use smallest u for each frequency range
n=0 for FR1
n=2 for FR2
For a CBW, GB for the CBW with 15kSCS is used in FR1, GB for the CBW with 60kSCS is used in FR2
  For a CBW not supporting 15kSCS in FR1, GB for the CBW with 30kSCS is used
  For a CBW not supporting 60kSCS in FR2, GB for the CBW with 120kSCS is used

## Slide 8
Issue 3: SCS selection (Cont’d)
Agreement:
Option 1: maximum u supporting both CBW1 and CBW2

## Slide 9: Reference
R4-1905894 Definition of nominal channel spacing for CA, Intel
R4-1906629 Nominal channel spacing for CA and definition of contiguous/non-contiguous CA , Nokia, Nokia Shanghai Bell
R4-1906630 Threshold for no-contiguous CA spacing for FR1, Nokia
R4-1906631 Threshold for no-contiguous CA spacing for FR2, Nokia
R4-1906632 Threshold for no-contiguous CA spacing, Nokia
R4-1906633 CA nominal channel spacing alignment among sub-carrier spacing for FR1, Nokia
R4-1906634 CA nominal channel spacing alignment among sub-carrier spacing for FR2, Nokia
R4-1906635 CA nominal channel spacing alignment among sub-carrier spacing, Nokia
R4-1906806 Nominal channel spacing related signaling information, ZTE
R4-1905240 Way forward on channel spacing, ZTE

## Slide 10: Reference(Cont’d)
R4-1906112 Further discussion on the Nominal channel spacing for CA, ZTE
R4-1906113 Draft CR to TS 38.101-1: Nominal channel spacing for NR, ZTE
R4-1906114 Draft CR to TS 38.101-2: Nominal channel spacing for NR, ZTE
R4-1906115 Draft CR to TS 38.104: Nominal channel spacing for NR, ZTE
R4-1906116 CR to TS37.104: Nominal channel spacing for NR for CA , ZTE
R4-1906117 CR to TS37.141: Nominal channel spacing for NR for CA , ZTE
R4-1906265 Correction to CA carrier spacing Ericsson
R4-1906266 Correction to CA carrier spacing Ericsson
R4-1906267 Correction to CA carrier spacing Ericsson
R4-1906381 on nominal channel space for CA Huawei, HiSilicon