## Slide 1: WF on NR V2X UE transmit timing error
LG Electronics, [...]
3GPP TSG-RAN WG4 #91 Meeting
Reno, US, 13th– 17th May, 2019
R4-1907729

## Slide 2
RAN4 RF agreement for Co-existence Scenario
  Scenarios for ITS spectrum in RAN4 #90bis
  Scenarios for Licensed band with SL operation in RAN4#91
    NR V2X UE to NR Uu BS/UE
    NR V2X UE to LTE Uu BS/UE
    NR Uu UE to NR V2X UE
    LTE Uu UE to NR V2X UE
  the example bands will be
    Option 1: 2GHz (Uplink part of a FDD band 1 and band 3)
    Option 2: 3.5GHz (TDD bands)
    Option 3: 28GHz (FR2)
Other candidate scenarios for inter-band concurrent operation
    - NR Uu + NR V2X SL(ITS)
    - LTE Uu + NR V2X SL(ITS)
Background

## Slide 3
RAN1 agreements
  On synchronization mechanism,
    11 RBs for S-SSB BW
    Length-127 M-sequence for S-PSS & Length-127 Gold sequence for S-SSS, 2 symbols for each of S-PSS and S-SSS
  Support of LTE PC5 scheduling by NR Uu (mode 3-like ) is based on UE capability
    NR Uu + LTE V2X SL(ITS)
  SL SCS
    SL RxSCS = SL TxSCS
    DL RxSCS can be different from SL TxSCS for inter-band con-cocurrent operation
    DL RxSCS = SL TxSCS has been discussing for NR V2X in shared Licensed band (UL TxSCS = SL TxSCS)
Background

## Slide 4
RRM requirements should be specified by considering the following NR V2X SL operation
  NR V2X SL in ITS band (FR1)
  NR V2X SL in Licensed band for FR1 & FR2
    - Need to discuss FR2 with 2nd priority
  Inter-band con-current operation
    1st priority
      NR Uu + NR V2X(ITS)
      LTE Uu + NR V2X(ITS)
    2nd priority
      NR Uu + LTE V2X(ITS)
      Current WID does not include related RAN4 work.
WF

## Slide 5
For NR V2X SL Tx timing error
  - the following synchronization reference sources should be considered based on RAN1 agreement for SL SCS relationship in Background.
    - GNSS
    - gNB
    - eNB
    - NR UE
  On top of timing error by each synchronization reference source at reception side, additional timing error which depends on different SCS of transmit SL should be considered
  RAN4 encourage interest companies to provide NR V2X SL Tx timing error and methodologies assumed for each synchronization reference source in next meeting
  Send reply LS on NR V2X SL Tx timing error to RAN1 in RAN4#92
WF