## Slide 1: WF on NR V2X UE transmit timing error
LG Electronics, [...]
3GPP TSG-RAN WG4 #91 Meeting
Reno, US, 13th– 17th May, 2019
R4-1907731

## Slide 2
RAN4 RF agreement for Co-existence Scenario
  Scenarios for ITS spectrum in RAN4#91
  Scenarios for Licensed band with SL operation in RAN4#91
    NR V2X UE to NR Uu BS/UE
    NR V2X UE to LTE Uu BS/UE
    NR Uu UE to NR V2X UE
    LTE Uu UE to NR V2X UE
Other candidate scenarios for inter-band concurrent operation
    - NR Uu + NR V2X SL(ITS)
    - LTE Uu + NR V2X SL(ITS)
Background

## Slide 3
RAN1 agreements
  On synchronization mechanism,
    11 RBs for S-SSB BW
    Length-127 M-sequence for S-PSS & Length-127 Gold sequence for S-SSS, 2 symbols for each of S-PSS and S-SSS
  Support of LTE PC5 scheduling by NR Uu (mode 3-like ) is based on UE capability
    NR Uu + LTE V2X SL(ITS)
Background

## Slide 4
RAN1 agreements
  SL SCS
    Confirm the working assumption
      Working assumption: only one SL BWP is configured in a carrier for a NR V2X UE
    BWP is defined for NR sidelink.
      The same SL BWP is used for both Tx and Rx.
      Numerology is a part of SL BWP configuration
    Configuration for SL BWP is separated from Uu BWP configuration signalling.
      UE is not expected to use different numerology in the configured SL BWP and active UL BWP in the same carrier at a given time.
        FFS the time scale
        FFS relation to DL BWP including initial Uu BWP
        FFS relation in terms of frequency location and bandwidth
Background

## Slide 5
RRM requirements should be specified based on the scenarios agreed in the RAN4 RF group.
WF

## Slide 6
For NR V2X SL Tx timing error
  - the following synchronization reference sources should be considered based on RAN1 agreement.
    GNSS
    gNB
    eNB
    NR UE
    RAN4 shall study the impact of synchronization source selection if any of eNB and gNB can be used as sync source based on the conclusion of RAN4 RF or RAN1.
  On top of timing error by each synchronization reference source at reception side, additional timing error should be considered, e.g., error depends on different SCS of transmit SL
  For next meeting, companies are encouraged to present provide their views on:
    Methodology used for deriving the NR V2X SL Tx timing error requirement
    NR V2X SL Tx timing error
RAN4 shall study impact of BWP switching in NR Uu (DL/UL) on NR SL.
WF