## Slide 1: 3GPP TSG-RAN WG4 Meeting #91 Reno, United States of America, 13 – 17 May, 2019
Ericsson, Nokia, Nokia Shanghai Bell , Qualcomm Incorporated, Huawei, HiSilicon, Sierra Wireless, S.A.
Way forward on Rel-16 MTC RRM enhancement
R4-1907733

## Slide 2: Wake-up signal
In release 16, release 15 WUS reception requirements apply for release 15 UE.
RAN4 shall wait for further RAN1 progress related to WUS design, and shall disusss whether it is possible to reuse the Rel-15 WUS reception requirements at RAN4#92 meeting.

## Slide 3: MPDCCH performance improvement for RLM
RAN4 shall wait for further RAN1 progress related to MPDCCH design (e.g. precoder options)
  RAN4 shall aim to agree on simulation assumptions based on further progress on MPDCCH design at RAN4#92 meeting conditioned on RAN1 progress.
  RAN4 shall then start evaluating the MPDCCH BLER performance based on the agreed simulation assumptions.

## Slide 4: Preconfigured UL resource
When TA validation based on serving cell RSRP change method is configured:
  eNodeB determines and configures K RSRP threshold(s) to the UE, where K is 1 or 2.
  It is FFS whether relaxed serving cell monitoring shall not be allowed when the signaled relaxation factor N is ≥ X, where X > 1. The value of X is FFS.
PUR transmission:
  UE shall transmit in the PUR transmission opportunity using the obtained TA
    If UE is synchronized towards the serving cell before PUR opportunity
    Otherwise, UE may postpone the transmission to the next intended PUR transmission opportunity according to higher layer request of the UE or network configuration after UE has obtained the synchronization towards the serving cell within Tsearch, or it may drop the transmission.
        Tsearch =the time required for PSS/SSS acquisition in eDRX. In DRX, Tsearch is the time required for performing tracking loop and exact duration is FFS.

## Slide 5: Mobility enhancement
RSS based RSRP measurement yields better measurement performance compared to CRS based under certain side conditions
  The side conditions for the scenarios where RSS is to be used is FFS.
RSS based RSRP measurement may be used for CE level selection when multiple CE levels are configured in RA.
RSS based RSRP measurement for neighbor cells are pending RAN1/RAN2 agreements on RSS configurations.
Companies are encouraged to provide simulation results for:
  2 Rx case
  1, 2 and 3 samples averaging assuming a measurement period of 160, 320 and 480 ms.

## Slide 6: DL quality reporting
RAN4 shall wait for further RAN1/RAN2 progress.