## Slide 1: 3GPP TSG-RAN WG4 Meeting #91 Reno, USA, 13th – 17th May 2019
Huawei, HiSilicon, Nokia, Ericsson, Qualcomm
Way forward on R16 enhancement for NB-IoT RRM
R4-1907734

## Slide 2: Group WUS
In release 16, release 15 WUS reception requirements apply for release 15 UE.
RAN4 shall wait for further RAN1 progress related to WUS design, and shall disusss whether it is possible to reuse the Rel-15 WUS reception requirements at RAN4#92 meeting.

## Slide 3: Preconfigured UL resource
When TA validation based on serving cell NRSRP change method is configured:
  eNodeB determines and configures K NRSRP threshold(s) to the UE, where K is 1 or 2.
  It is FFS whether relaxed serving cell monitoring shall not be allowed when the signaled relaxation factor N is ≥ X, where X > 1. The value of X is FFS.
PUR transmission:
  UE shall transmit in the PUR transmission opportunity using the obtained TA
    If UE is synchronized towards the serving cell before PUR opportunity
    Otherwise, UE may postpone the transmission to the next intended PUR transmission opportunity according to higher layer request of the UE or network configuration after UE has obtained the synchronization towards the serving cell within Tsearch, or it may drop the transmission.
        Tsearch =the time required for NPSS/NSSS acquisition in eDRX. In DRX, Tsearch is the time required for performing time tracking and exact duration is FFS.

## Slide 4: NRS presence on non-anchor carriers
For NRSRQ measurement on non-anchor carriers
  NRSRQ measurements on a non-anchor paging carrier cannot be translated to the equivalent NRSRQ measurements of the anchor carrier in the same way that NRSRP can be translated.
  RAN4 is further investigating possible alternative methods for NRSRQ measurements translation between non-anchor paging and anchor carriers
It is FFS whether serving cell measurement relaxation introduced in Rel 15 for WUS can also be applied when the UE performs serving cell measurements on the non-anchor paging carrier

## Slide 5: Msg3 based channel quality reporting
FFS whether T1 defined in R14 applies for MSG3 DL quality report in non-anchor carriers
RAN4 shall take into account further RAN1/RAN2 progress on reporting message type details