## Slide 1: Way forward on RRM enhancement for LTE HST
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #91
Reno, United States of America, 13 - 17 May, 2019
R4-1907739
Document for: Approval

## Slide 2: Target velocity of RAN4 RRM requirements
In Rel-16 the target velocity for SCC RRM requirements for high speed enhancement is 350km/h, and the target velocity for PCC RRM requirement (single carrier mode) is 500km/h.
Maximum Doppler shift in RRM simulations is limited to 972Hz, following the agreed UE demodulation assumption on Doppler limitation.

## Slide 3: SCell measurement(1)
Measurement requirements for active SCell (target speed is 350km/h)
  The same number of samples as the measurement requirement for PCell in Rel-14 can be reused for SCell measurement requirement in Rel-16.
Measurement requirements for deactivate SCell (target speed is 350km/h)
  When common DRX is used:
    Tidentify_intra = max (10 * measCycleSCell, Tidentify_scc1_enhancement)
    Tmeasure_intra = max (3 * measCycleSCell, Tmeasure_scc1_enhancement).
    Tidentify_scc1_enhancement and Tmeasure_scc1_enhancement are specified as following table:
DRX cycle length (s) | Tidentify_scc1_enhancement (s) (DRX cycles) | Tmeasure_scc1_enhancement (s) (DRX cycles)
≤0.04 | 0.8 (Note1) | 0.2 (Note1)
0.04<DRX-cycle≤0.08 | Note2(15) | Note2 (4)
0.08<DRX-cycle≤1.28 | Note2(10) | Note2 (3)
1.28<DRX-cycle≤2.56 | Note2(20) | Note2 (5)
Note1: Number of DRX cycle depends upon the DRX cycle in use Note2: Time depends upon the DRX cycle in use |  | 

## Slide 4: SCell measurement(2)
When no common DRX is used
  Tidentify_intra = 10 * measCycleSCell
  Tmeasure_intra = 3 * measCycleSCell

## Slide 5: SCell activation delay
Option 1(Intel):
  No MBSFN subframe is applicable for SCell activation delay in LTE high speed scenario.
Option 2(Quacomm, Ericsson, Huawei, NTT DOCOMO):
  No enhancement is needed

## Slide 6: PCell cell reselection requirements in idle mode
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 2.24 (7) | 0.32(1) | 0.64(2)
0.64 | 4.48 (7) | 0.64 (1) | 1.28(2)
1.28 | 8.96(7) | 1.28 (1) | 2.56 (2)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 3.2 (10) | 0.32(1) | 0.96(3)
0.64 | 6.4 (10) | 0.64 (1) | 1.92 (3)
1.28 | 7.68(6 or other value) | 1.28 (1) | 3.84 (3)
2.56note1 | 58.88 (23) | 2.56 (1) | 7.68 (3)
Note1: The DRX configuration is not applicable for high speed scenario. |  |  | 
Option 1(Ericsson)
Option 2(Huawei, Intel)
Other options are not precluded.

## Slide 7
Option 1(Ericsson, Qualcomm, Nokia, Intel):
  No enhancement is needed
Option 2(Huawei, Intel)
PCell measurement requirements
in connected mode with DRX
DRX cycle length (s) | Tidentify_intra (s) (DRX cycles)
≤0.04 | 0.8 (Note1)
0.04<DRX-cycle≤0.08 | Note2(15)
0.08<DRX-cycle<1.28 | Note2(10)
DRX=1.28 | Note2 (6 or larger value)
1.28<DRX-cycle note3≤2.56 | Note2(20)
Note1: Number of DRX cycle depends upon the DRX cycle in use. Note2: Time depends upon the DRX cycle in use. Note3: The DRX configuration is not applicable for high speed scenario. | 

## Slide 8: PCell measurement requirements in connected mode without DRX
No enhancement is needed

## Slide 9: UL Timing
The value of Tq
  The maximum autonomous timing adjustment step Tq (per 200ms) for up to 500km/h is suggested to be defined as follows:
Downlink Bandwidth (MHz) | Tq_
1.4 | 17.5*TS
3 | 9.5*TS
5 | 5.5*TS
Note: TS is the basic timing unit defined in TS 36.211 | 

## Slide 10: RLM
Option 1(Intel):
  For RLM in high speed scenario, define a new event according to some threshold Qout,E1 which is less than 10%. A new signalling will be introduced for UE to indicate network that it is going to be out-of-sync if PDCCH block error rate is above Qout,E1.
Option 2(Intel):
  For RLM in high speed scenario, define the threshold Qout_HST as the level at which the downlink radio link cannot be reliably received and shall correspond to [10]% block error rate of a hypothetical PDCCH transmission with transmission parameters specified.
Option 3 (Ericsson):
  RAN4 specify RLM requirements only for the condition PDCCH is transmitted with transmission diversity when the new very high speed signalling is indicated.
Option 4 (Qualcomm, Huawei)
  No enhancement is needed
Companies are encouraged to provide simulation results in next meeting.

## Slide 11: Capability and Configuration Signalling
Two additional capabilities and configuration flags are added in release 16 to
  Indicate and enable support for SCell enhancements in cDRX and for deactivated SCells supporting up to 350km/h velocity
  Indicate and enable support for PCell enhancements supporting higher UE speed than 350km/h (only consider non-CA case)
Send LS to RAN2 based on above agreements.