## Slide 1: Way forward on Rel-16 LTE HST BS demodulation requirements
3GPP TSG-RAN WG4 Meeting #91
Reno, Nevada, USA, 13 – 17 May 2019
Agenda item: 7.15.5 BS Demodulation [LTE_high_speed_enh2-Perf]
Document for: Approval
R4-1907747
Nokia, Nokia Shanghai Bell, NTT DOCOMO, INC., Ericsson

## Slide 2: Background
In RAN4 #91, BS performance requirements for high speed were discussed based on contributions [1-4]

## Slide 3: WF on PUSCH for HST for evaluation (not for requirement)
Deployment scenarios and related parameters (e.g., Ds, Dmin, fd) will be decided based on evaluation results. The following parameters should be considered in the evaluation.
Maximum Doppler shift will be based on the outcome of simulation results and could be less than 2 times downlink Doppler shift.
Note: This agreement does not exclude work on unidirectional scenario.
Parameter | Value |  |  | 
 | Open space |  | Tunnel for multi-antennas | 
 | Bi-directional (1st priority) | Uni-directional | Bi-directional (1st priority) | Uni-directional
Ds | 1000 m |  | 300 m | 
Dmin | 50 m |  | 2 m | 
v | 500 km/h (lower speeds are not precluded) |  | 500 km/h (lower speeds are not precluded) | 
fd | 1944 Hz, 1894 Hz, 1844 Hz, 1794 Hz, 1744 Hz, 1694 Hz |  |  | 

## Slide 4: WF on PUSCH for HST for evaluation (not for requirement)
Initial simulation assumption for just information
Parameters | Unit | Values
Bandwidth | MHz | 10
MCS for PUSCH |  | QPSK 1/2 1/3 16QAM 3/4
Propagation condition and correlation matrix |  | Reference to the previous slide
Antenna configuration |  | 1x2
Reference receiver |  | MRC
Noise estimation |  | Practical
Time and frequency track |  | Practical

## Slide 5: Reference
[1] R4-1907002, BS demodulation for LTE high speed in Rel.16, NTT DoCoMo Inc., RAN4#91
[2] R4-1905441, Discussion and simulation results for BS performance with HST in LTE Rel-16” Samsung, RAN4#91
[3] R4-1906912, Preliminary BS demodulation results under bi-directional scenarios for Rel-16 LTE HST, Nokia, Nokia Shanghai Bell, RAN4#91
[4] R4-1906952, Analysis of Doppler Shift Observed by Base Station in HST, Qualcomm, RAN4#91