## Slide 1: WF for n7 new channel bandwidths
Nokia, Qualcomm, Huawei
R4-1907782

## Slide 2: Background
In order to introduce new channel bandwidths for n7 A-MPR and REFSENS needs to be specified.
REFERENCES
[1] R4-1905337, n7 new channel BW REFSENS, Nokia, RAN4#91
[2] R4-1907168, n7 new channel bandwidths AMPR for B38 protection, Qualcomm Incorporated, Nokia RAN4#91
[3] R4-1903857, Further consideration on UE reference sensitivity requirements on adding wider channel bandwidths in Band n7, Huawei, HiSilicon, , Nokia RAN4#90bis
[4] R4-1900067, n7 new channel bandwidths emissions study, Nokia,RAN4#90
[5] R4-1900894, UE reference sensitivity requirements on adding wider channel bandwidths in Band n7, Huawei, HiSilicon, RAN4#90

## Slide 3: A-MPR
Based on input from [2] and [4] following A-MPR is agreed
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
25 MHz | 2534.5 ≤ FC < 2557.5 |  | Note 1 | A3
30 MHz | 2515 ≤ FC ≤ 2555 | ≥0, <1.44 | >0 | A4
 |  | ≥1.44, <13.5 | >max (0, 12*SCS*RBend -1.8) | A5
 |  | ≥13.5, <19.8 | >11.52 | A6
 |  | ≥19.8, <25.92 | >6.3 | A7
 |  | ≥25.92 | >0 | A8
40 MHz | 2520 ≤ FC ≤ 2550 | ≥0, <4.14 | >0 | A4
 |  | ≥4.14, <18 | >max (0, 12*SCS*RBend - 4.5) | A5
 |  | ≥18, <25.74 | >13.5 | A6
 |  | ≥25.74, <32.4 | >12.6 | A7
 |  | ≥32.4 | >0 | A8
50 MHz | 2525 ≤ FC ≤ 2545 | ≥0, <9 | >0 | A4
 |  | ≥9, <21.6 | >max (0, 12*SCS*RBend - 7.2) | A5
 |  | ≥21.6, <31.5 | >18 | A6
 |  | ≥31.5, <39.6 | >16.2 | A7
 |  | ≥39.6 | >0 | A8
Note 1: >9.72MHz for DFT-s-OFDM, >16.02MHz for CP-OFDM. CP-OFDM threshold only applies for 20 and 25MHz bandwidths. |  |  |  | 
Modulation/Waveform |  | A3 | A4 | A5 | A6 | A7 | A8
 |  | Outer | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner
DFT-s-OFDM | PI/2 BPSK | [4.5] | [5] | [2] | [3.5] | [6] | [10]
 | QPSK | [4.5] | [5] | [2] | [3.5] | [6] | [10]
 | 16 QAM | [4.5] | [5] | [2] | [3.5] | [6] | [10]
 | 64 QAM | [4.5] | [5] |  | [3.5] | [6] | [10]
 | 256 QAM |  |  |  |  | [6] | [10]
CP-OFDM | QPSK | [6] | [5] | [3.5] | [5.5] | [7] | [11]
 | 16 QAM | [6] | [5] | [3.5] | [5.5] | [7] | [11]
 | 64 QAM | [6] | [5] | [3.5] | [5.5] | [7] | [11]
 | 256 QAM | [6] |  |  |  | [7] | [11]

## Slide 4: REFSENS
Based on input from [1], [3] and [5] following REFSENS is agreed
Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) |  | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm)
n7 | 15 | -98.0 | -94.8 | -93.0 | -91.8 |  | -90.7 | -89.9 | -88.6 | [-77.6]
 | 30 |  | -95.1 | -93.1 | -92.0 |  | -90.8 | -90.0 | -88.7 | [-77.7]
 | 60 |  | -95.5 | -93.4 | -92.2 |  | -91.0 | -90.1 | -88.9 | [-77.8]
Table 7.3.2-1: Two antenna port reference sensitivity QPSK PREFSENS
Table 7.3.2-3: Uplink configuration for reference sensitivity (from 38.101-1)
Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | Duplex Mode
n7 | 15 | 25 | 501 | 751 | 751 | 721 | 641 | 451 | 451 | FDD
 | 30 |  | 24 | 361 | 361 | 361 | 321 | 201 | 201 | 
 | 60 |  | 101 | 18 | 181 | 181 | 161 | 101 | 101 | 
NOTE 1: 1 Refers to the UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission bandwidth configuration for the channel bandwidth (Table 5.3.2-1).