## Slide 1: Draft WF on FR1/FR2 difference
R4-1907803
Ericsson, Huawei

## Slide 2: Introduction
This WF captures differences between FR1 and FR2 requirements for different areas of the 3GPP specifications
The list is not exhaustive and further aspects may be added in future
The list should be elaborated into further detail of what are the implications for FR1, FR2.

## Slide 3: RAN1
38.211: FR1/FR2: 7/6 occurrences. Random access configuration depends on FR1/FR2. Transition times RXTX and TXRX depend on FR1/FR2. offsetToPointA unit depends on FR1/FR2.
38.212: FR1/FR2: 0/0 occurrences
38.213: FR1/FR2: 38/23 occurrences. SSB pattern and cell search depend on FR1/FR2. Power control aspects for dual connectivity depend on FR1/FR2. BWP switching in RA procedure depends on FR1/FR2. Actions related to bwp-InactivityTimer in BWP switching depend on FR1/FR2. Type0-PDCCH monitoring behavior depends on FR1/FR2.
38.214: FR1/FR2: 9/8 occurrences. Different behavior w.r.t. overlapping reception of unicast PDSCH and SI-PDSCH. FR2 supports TRS in single slot. PT-RS support is different w.r.t. FR1/FR2. PDSCH and PUSCH processing capability 2 is only defined for FR1. FR1 supports almost contiguous allocation for UL CP- OFDM while FR2 does not.

## Slide 4: RAN2
UE capability signaling differs
Interpretation of DL signaling differs
The terms "FR1"/"FR2" are mentioned 106/81 times in 38.331 (RRC) and 93/95 times in 38.306 (UE Capabilities).
Signaling relating to SCS, BW, RAN1 procedures impacted

## Slide 5: RAN4 BS RF
Concept of OTA requirements and declarations
  For FR1 there is a fundamental link between OTA requiremenst and OTA coverage area with the intention of maintaining equivalence with the conducted requirements.
    For FR1, the widest beam needs to cover the whole cell as there is no beam sweeping, whereas for FR2 the widest beam is likely to be narrower (however the specification treats the beam declarations in the same manner)
    FR1 Reciever has 2 reference sensitivity declarations, OTA reference sentitivity is itended to ensure equivalence with the conducted requirements.
  FR2 has no link between OTA requirements and coverage, OTA requirements are based on highest gain beam forming.
Type of testing (FR1: -C, -H, -O FR2 –O only)
Scope of requirements (co-location and some others)
Absolute level for some requirements is FR dependent

## Slide 6: RAN4 UE RF
Type of testing
Concept of some requirements (needs to be elaborated)

## Slide 7: RAN4 RRM
Handover delay etc. Requirements considering beam sweeping for FR2, but not for FR1
Beamsweeping restrictions due to BS being unable to simultaneously beamform towards the serving cell and sweep for FR2, not applicable for FR1.
Measurement capabilities differ between FR1 and FR2