## Slide 1: Way forward on new capability sets
R4-1907807, Ericsson, Huawei, Nokia, Nokia Shanghai Bell, ZTE

## Slide 2: Way Forward on New Capability Sets
Introduce the following Capability Sets:
  CS18 GSM+E-UTRA+NR
  CS19 UTRA+E-UTRA+NR
  [CS20 GSM + UTRA + E-UTRA + NR]
Add a statement in the conformance specification that if two or more CS are supported, duplicated tests only need to be performed once.
For CS20, decide whether or not to include considering:
  Whether conformance for all RATs in a band is clear
  If CS20 is included, testing of CS20 is a combination of CS18 and CS 19 testing
    Tests defined for each configuration are performed only once

## Slide 3
Capability Set supported by the BS | CS18 | CS19
Supported RATs | GSM, E-UTRA3, NR | UTRA, E-UTRA3, NR
Supported configurations | SR E-UTRA3 (SC, MC, CA) SR NR (SC, MC, CA) MR GSM + E-UTRA3 MR GSM + NR MR E-UTRA3 + NR MR GSM+ E-UTRA3 + NR | SR UTRA (SC, MC) SR E-UTRA3 (SC, MC, CA) SR NR (SC, MC, CA) MR UTRA + E-UTRA3 MR UTRA + NR MR E-UTRA3 + NR MR UTRA + E-UTRA3 + NR
Applicable BC | BC2 | BC1, BC2
NOTE 1: MC denotes multi-carrier in single RAT; SC denotes single carrier; MR denotes multi-RAT; SR denotes single-RAT. NOTE 2: For this configuration related to BC2 bands, the support of UTRA in band 3 is declared by the manufacturer. NOTE 3: Includes optional (declared by the manufacturer) support of NB-IoT in-band and/or NB-IoT guard band operation. |  | 

## Slide 4
[CS 204]
GSM4, UTRA4, NR, E-UTRA, NB-IoT in-band3, NB-IoT guard band
MR GSM + E-UTRA3 + NR MR GSM + NR MR GSM + E-UTRA3 SR E-UTRA3 (SC, MC, CA) MR UTRA + E-UTRA3 + NR MR E-UTRA3 + NR MR UTRA + NR MR UTRA + E-UTRA3 SR NR (SC, MC, CA) SR E-UTRA3 (SC, MC, CA) SR UTRA (SC, MC)
NOTE 1: MC denotes multi-carrier in single RAT; SC denotes single carrier; MR denotes multi-RAT; SR denotes single-RAT. NOTE 2: For this configuration related to BC2 bands, the support of UTRA in band 3 is declared by the manufacturer. NOTE 3: Includes optional (declared by the manufacturer) support of NB-IoT in-band and/or NB-IoT guard band operation within E-UTRA carrier(s) NOTE 4:. GSM and UTRA are transmitted from different connectors if transmitted simultaneously.
Note: CS20 is applicable to BC2.