## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26th – 30th August 2019
Huawei, HiSilicon, …
Way forward on the variable duplex
R4-1908737

## Slide 2: Background
It is agreed in the WID to consider the following aspects
  The operating duplex mode shall be “Variable duplex FDD”, given that the uplink and downlink blocks may have been licensed independently and shall be operable simultaneously by the UE
  Uplink sharing operation of the NR uplink carrier with an LTE uplink carrier
    from network perspective in case of standalone operation
    from UE perspective (ULSUP-TDM and ULSUP-FDM) in case of EN-DC operation
  Base station RF requirements shall take into account the presence of an additional downlink LTE carrier, given that the uplink may be operating on a licensed band where downlink is used by other RATs
  The individual EN-DC band-combinations corresponding to the above bands, to which the new core requirements will be applied, will be progressed as part of the EN-DC band combinations Release 16 basket WI, and also have Release independence from Rel-15

## Slide 3: Way forward
For system parameters of the new bands, specify in both TS 38.101-1 and TS 38.104
  the new FDD bands: n91, n92, n93 and n94, and
  the channel raster and sync raster per new FDD bands, and
  the supported channel BW and supported SCS for the new FDD bands
NR Operating band | ΔFRaster (kHz) | Uplink Range of NREF (First – <Step size> – Last) | Downlink Range of NREF (First – <Step size> – Last)
n91 | 100 | 166400 – <20> – 172400 | 285400 – <20> – 286400
n92 | 100 | 166400 – <20> – 172400 | 286400 – <20> – 303400
n93 | 100 | 176000 – <20> – 183000 | 285400 – <20> – 286400
n94 | 100 | 176000 – <20> – 183000 | 286400 – <20> – 303400
NR Operating band | SS Block SCS | SS Block pattern1 | Range of GSCN (First – <Step size> – Last)
n91 | 15 kHz | Case A | 3572 – <1> – 3574
n92 | 15 kHz | Case A | 3584 – <1> – 3787
n93 | 15 kHz | Case A | 3572 – <1> – 3574
n94 | 15 kHz | Case A | 3584 – <1> – 3787
NR Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz
n91 | 15 | Yes | Yes |  |  | 
 | 30 |  |  |  |  | 
 | 60 |  |  |  |  | 
n92 | 15 | Yes | Yes | Yes | Yes | 
 | 30 |  | Yes | Yes | Yes | 
 | 60 |  |  |  |  | 
n93 | 15 | Yes | Yes |  |  | 
 | 30 |  |  |  |  | 
 | 60 |  |  |  |  | 
n94 | 15 | Yes | Yes | Yes | Yes | 
 | 30 |  | Yes | Yes | Yes | 
 | 60 |  |  |  |  | 
NR operating band | Uplink (UL) operating band BS receive / UE transmit FUL,low – FUL,high | Downlink (DL) operating band BS transmit / UE receive FDL,low – FDL,high | Duplex Mode
n91 | 832 MHz – 862 MHz | 1427 MHz – 1432 MHz | FDD1
n92 | 832 MHz – 862 MHz | 1432 MHz – 1517 MHz | FDD1
n93 | 880 MHz – 915 MHz | 1427 MHz – 1432 MHz | FDD1
n94 | 880 MHz – 915 MHz | 1432 MHz – 1517 MHz | FDD1
Note 1: Variable duplex bands. |  |  | 

## Slide 4: Way forward
Specify the UE default TX-RX separation values for the new bands
Asymmetric channel BW operation should be supported with below combinations:
It is mandatory for the UE to support 7.5kHz shift to operate in the new bands n91, n92, n93 and n94 in variable duplex FDD
Consider in the band combinations with regard to the new bands in the future that
  The UE supports UL sharing from UE perspective (either TDM or FDM) when operating in EN-DC combinations with the variable duplex FDD bands
  The network supports UL sharing from network perspective when operating with the variable duplex FDD bands
Band | Minimum supported BW | Default TX-RX separation
n91 | 5MHz | 570MHz
n92 | 5MHz | 575MHz
n93 | 5MHz | 517MHz
n94 | 5MHz | 522MHz
NR Operating Band | Channel BWs for UL (MHz) | Channel BWs for DL (MHz)
n91 | 10 | 5
n92 | 5 | 10, 15, 20
 | 10 | 15, 20
n93 | 10 | 5
n94 | 5 | 10, 15, 20
 | 10 | 15, 20