## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26th – 30th Aug 2019
Huawei, HiSilicon
Way forward on RRM impact of the R16 enhancement for NB-IoT
R4-1909013

## Slide 2: Group WUS
Rel-15 WUS requirement metric can be re-used, except that ,
  99% detection probability applies for each of the WUS sequence UE is monitoring, and
  1% / N false detection probability applies for each of the WUS sequence UE is monitoring
RAN4 to discuss and decide the assumptions for Rel-16 UE requirements in terms of number of WUS sequences to monitor and the existence of other WUS sequences

## Slide 3: Preconfigured UL resource
It is up to network implementation to use 1 or 2 threshold(s) for RSRP change based TA validation
Relaxed serving monitoring is allowed when serving cell RSRP change based TA validation is used
RAN4 should specify the Tx timing requirement for PUR transmission, which should be same as PUSCH transmission in connected mode. RAN4 not to define any synchronization requirement (time to achieve synchronization) related to PUR transmission
The UE is required to take NRSRP measurement for NRSRP change TA validation, if configured, during the warm up period of the PUR occasions

## Slide 4: Multi carrier operation non-anchor RRM
RAN4 decides that for the measurement samples from a single carrier,
  Option 1: the UE is allowed to translate the RSRP results from non-anchor filtered results to anchor carrier by the corresponding RSRP offset value configured by the network and skip RSRQ evaluation
  Option 2: provide carrier specific Qrxlevmin and Qqualmin for carrier specific S-criteria
RAN4 decides that for the measurement samples from different carriers,
  Option 1: the UE is allowed to translate the RSRP results from non-anchor samples to anchor ones by the corresponding RSRP offset value configured by the network and skip RSRQ evaluation
  Option 2: the results are not feasible
Any filtered results, either from anchor or non-anchor carrier, can trigger neighbor cell measurement and/or relaxed monitoring abortion
A threshold should be used so that if the two samples of measured RSRP and/or RSRQ are spaced by a period longer than the threshold the results do not count

## Slide 5: Multi carrier operation connected channel quality report
For connected mode channel quality reporting, the UE is allowed to report after msg5 the channel quality of the msg5 carrier within the below values,
  in non-DRX cases, 800ms for normal coverage and 1600ms for enhanced coverage;
  in DRX cases, 5 DRX cycles
Measurement report mapping for connected channel quality reporting should follow that of msg3-based measurement report mapping