## Slide 1: Way forward on NR PDSCH demodulation requirements for CA, EN-DC, NE-DC, and NR-DC
Ericsson
3GPP TSG-RAN WG4 Meeting #92
Ljubljana, Slovenia, 26 – 30 August, 2019
R4-1909167

## Slide 2: PDSCH CA requirements with 2CC
RAN4 specifies NR 2CC PDSCH demodulation requirements with the following combinations:
Test number | Frequency range | CA type | Duplex mode | SCS
1 | FR1 | Intra-band Contiguous CA | FDD+FDD | 15kHz + 15kHz
2 | FR1 | Intra-band Contiguous CA | TDD+TDD | 30kHz + 30kHz
3 | FR1 | Intra-band Non-contiguous CA | TDD+TDD | 30kHz + 30kHz
4 | FR1+FR1 | Inter-band CA | FDD+FDD | 15kHz + 15kHz
5 | FR1+FR1 | Inter-band CA | TDD+TDD | 30kHz + 30kHz
6 | FR1+FR1 | Inter-band CA | FDD+TDD | 15kHz + 30kHz
7 | FR2 | Intra-band Contiguous CA | TDD+TDD | 120kHz + 120kHz
8 | FR2 | Intra-band Non-contiguous CA | TDD+TDD | 120kHz + 120kHz
9 | FR1+FR2 | Inter-band CA | FDD+TDD | 15kHz + 120kHz
10 | FR1+FR2 | Inter-band CA | TDD+TDD | 30kHz + 120kHz

## Slide 3: PDSCH CA requirements with CC > 2
RAN4 specify the PDSCH demodulation requirements with CC > 2 according to the existing CA combinations specified or to be specified in TS38.101-1/2/3 in Rel-16.

## Slide 4: EN-DC/NE-DC/NR-DC test cases
EN-DC tests
  NR CA PDSCH demodulation requirements are also applicable for EN-DC tests
    Need also consider the specified band combinations in TS38.101-3.
NE-DC tests
  Introduce one NE-DC combination according to TS38.101-3
    NR: FR1 FDD (SCS=15kHz) single carrier
    LTE: FDD single carrier
NR-DC tests
  Introduce one NR-DC combination according to TS38.101-3
    FR1 TDD (SCS=30kHz) + FR2 TDD (SCS=120kHz)