## Slide 1: WF on RRM Requirements for NR-U
Ericsson
3GPP TSG-RAN WG4 Meeting #92 R4-1909463
Ljubljana, Slovenia, 26th – 30th August 2019
Agenda Item: 9.1.5

## Slide 2: Serving Cell Evaluation
The NR-U standalone UE shall measure and evaluate the cell selection criterion S for the serving cell at least once every (1+Ms)*M1*N1 DRX cycles in Nserv consecutive DRX, where
  M1=2 if DMTC periodicity (TDMTC) > 20 ms and DRX cycle ≤ 0.64 second, otherwise M1=1
  Nserv is as below
  N1 = rx beam related scaling as in existing requirements
  Maximum value of Ms is TBD
UE shall restart the measurements used for serving cell evaluation if it cannot fulfil the conditions on maximum number of DRS occasions (K) not available during the evaluation time, where the value of K is TBD
UE shall initiate measurements
  on neighbour cells indicated by the serving cell if it is unable to measure on the serving cell for at least M number of DRX cycles due to LBT failure, where the value of M is TBD
  on neighbour cells of any intra-frequency or inter-frequency if it is unable to measure on serving cell during at least M number of DRX cycles due to LBT failure regardless of any condition of SnonIntraSearchP and SnonIntraSearchQ
DRX cycle length [s] | Scaling Factor (N1) |  | Nserv [number of DRX cycles]
 | FR1 | FR2Note1 | 
0.32 | 1 | 8 | (1+Ms)*M1*N1*4
0.64 |  | 5 | (1+Ms)*M1*N1*4
1.28 |  | 4 | (1+Ms)*N1*2
2.56 |  | 3 | (1+Ms)*N1*2
Note 1: Applies for UE supporting power class 2&3&4. For UE supporting power class 1, N1 = 8 for all DRX cycle length. |  |  | 

## Slide 3: Cell Reselection
Requirements are defined as below and accounting for the number of configured DRS occasions in the target cell which are not available due to LBT
The maximum values of Md, Mm and Me are TBD
The UE shall restart the measurements if it cannot fulfil the conditions on maximum number of DRS occasions not available during the measurement time
The UE shall filter the measurement (e.g. SS-RSRP/SS-RSRQ) using at least 2 measurements which are separated in time by at least DRX/2 but not separated in time by more than Mn
DRX cycle length [s] | Scaling Factor (N1) |  | Tdetect,NR_Intra [s] {number of DRX cycles} | Tmeasure,NR_Intra [s] {number of DRX cycles} | Tevaluate,NR_Intra [s] {number of DRX cycles}
 | FR1 | FR2Note1 |  |  | 
0.32 | 1 | 8 | 0.32x(36+Md)xN1xM2 {(36+Md)xN1xN2} | 0.32x(4+Mm) xN1xM2 {(4+Mm)xN1xM2} | 0.32x(16+Me) x N1 x M2 {(16+Me)xN1xM2}
0.64 |  | 5 | 0.64x(28+Md) x N1 {(28+Md)xN1} | 0.64x(2+Mm) x N1 {(2+Mm)xN1} | 0.64x(8+Me) x N1 {(8+Me)xN1}
1.28 |  | 4 | 1.28x(25+Md) x N1 {(25+Md)xN1} | 1.28x(1+Mm) x N1 {(1+Mm)xN1} | 1.28x(5+Me) x N1 {(5+Me)xN1}
2.56 |  | 3 | 2.56x(23+Md) x N1 {(23+Md)xN1} | 2.56x(1+Mm) xN1 {(1+Mm)xN1} | 2.56x(3+Me) x N1 {(3+Me)xN1}
Note 1: Applies for UE supporting power class 2&3&4. For UE supporting power class 1, N1 = 8 for all DRX cycle length. Note 2: M2 = 1.5 if DMTC periodicity of measured intra-frequency cell > 20 ms; otherwise M2=1. |  |  |  |  | 

## Slide 4: Handover
The interruption time during handover procedure can be defined as:
  Tinterrupt = Tsearch*(1+ Md) + TIU*(1+ Mi) + 20+ T∆*(1+ M∆) ms
  Where Md ≤ K1, Mi ≤K2 and M∆≤ K3 and values of K1, K2 and K3 are FFS.

## Slide 5: Active BWP Switching
The PDSCH reception and/or PUSCH transmission on the new BWP may be delayed due to LBT failures in DL and/or in UL respectively
The basic time period over which the BWP switching occurs shall be the same as defined in the existing requirements
The impact of LBT failures on PDSCH reception or PUSCH transmission after the BWP switching needs further investigation
The duration of interruption on a serving cell in licensed band or unlicensed band or due to BWP switching on a licensed or unlicensed band can be based on the existing interruption requirements

## Slide 6: RRC Release with Redirection
The RRC release with redirection delay requirements when the NR target cell operates on a carrier in unlicensed band may be extended due to LBT failures in DL and/or in UL in the target cell
The RRC release with redirection delay for RRC redirection to the NR target cell on a carrier in unlicensed band can be derived by including the impact of LBT failures in DL and UL in the existing RRC release with redirection delay requirement in section 6.2.3.2.1, TS 38.133
The cell search time for target cell (on a carrier in unlicensed band) within the RRC release with redirection delay is shown below
Frequency range (FR) of target NR cell | Tidentify-NR
FR1 | MAX (680 ms, ([11] + L1) x TDMTC)
L1 is the number of DMTC occasions unavailable at the UE during the cell search period due to DL LBT failure in the target cell on a carrier belonging to an unlicensed band. | 

## Slide 7: RRC Re-Establishment
RRC re-establishment delay for RRC re-establishment on the target cell on a carrier in unlicensed band may be extended due to LBT failures in DL and/or in UL in the target cell
RRC re-establishment delay for RRC re-establishment to the target cell on a carrier in unlicensed band can be derived by including the impact of LBT failures in DL and UL in the existing RRC re-establishment delay requirements in section 6.2.1 of TS 38.133
The cell search times for intra-frequency target cell and inter-frequency target cell on carriers in unlicensed band within the RRC re-establishment delay are shown in table 1 and table 2 respectively below, where
  K1 = number of DMTC occasions unavailable at the UE during the intra-frequency cell search period due to DL LBT failure in the target cell
  K2,i = number of DMTC occasions unavailable at the UE during the inter-freq. cell search period due to DL LBT failure in the target cell of carrier i
Serving cell SSB Ês/Iot (dB) | Frequency range (FR) of target NR cell | Tidentify_intra_NR [ms] | 
 |  | Known NR cell | Unknown NR cell
≥ [-8] | FR1 | MAX (200 ms, ([5]+K1) xTDMTC) | MAX (800 ms, ([10]+K1) x TDMTC)
< [-8] | FR1 | N/A | (800+20*K1)Note1
Note 1: The UE is not required to successfully identify a cell on any NR frequency layer when TDMTC > 20 ms and serving cell SSB Ês/Iot < [-8] dB. |  |  | 
Serving cell SSB Ês/Iot (dB) | Frequency range (FR) of target NR cell | Tidentify_inter_NR, i [ms] | 
 |  | Known NR cell | Unknown NR cell
≥ [-8] | FR1 | MAX (200 ms, ([6]+K2,i)xTDMTC, i) | MAX (800 ms, ([13]+K2,i) x TDMTC, i)
< [-8] | FR1 | N/A | (800 + 20*K2,i)Note1
Note 1: The UE is not required to successfully identify a cell on any NR frequency layer when TDMTC,i > 20 ms and serving cell SSB Ês/Iot < [-8] dB. |  |  | 

## Slide 8: Beam Management
Extend the evaluation period of SSB and CSI-RS resources for beam failure detection, e.g.,
Extend the Evaluation period of SSB and CSI-RS resources for candidate beam detection, e.g.,
Specify the limit of LBFD and LCBD to avoid too long evaluation period
Configuration | TEvaluate_BFD_SSB (ms)
no DRX | max([50], ceil((5+LBFD)*P)*TSSB)
Configuration | TEvaluate_CBD_SSB (ms)
non-DRX, DRX cycle ≤ 320ms | ceil(([3]+LCBD)*P) * TSSB

## Slide 9: L1-RSRP measurement
Keep the same L1-RSRP accuracy requirements as licensed spectrum operation
Extend the L1-RSRP measurement period of SSB and CSI-RS resources, e.g.,
Specifies the limit of LL1-RSRP to avoid too long evaluation period
L1-RSRP measurement reporting is performed only when UE receive MSSB SSB samples and MCSI-RS CSI-RS samples during the measurement period
  If UE cannot skip the L1-RSRP reporting but UE does not receive a certain number of SSB and/or CSI-RS samples with the measurement period, UE report ‘not valid’
Configuration | TL1-RSRP_Measurement_Period_SSB (ms)
non-DRX | max(TReport, ceil((M+LL1-RSRP)*P)*TSSB)

## Slide 10: Measurement Gaps: Applicability
Gap patterns with MGL=6ms are suitable for measurements based on DRS
Applicability of MG patterns #0,#1, #4 and #5 for measurements based on DRS is confirmed
Applicability of MG patterns #2,#3 and #6-#11 for measurements based on DRS depends on the possibility of shorter than 5ms DRS transmission window.
No new MG pattern needs to be introduced for DRS based measurements

## Slide 11: Measurement Gaps: Scaling Factor
RAN4 discusses feasibility of a capability to measure NR-U bands with an independent gap pattern
Discussion of the capability to measure NR-U bands with an independent gap pattern can be done under the assumption that gap based FR2 measurements do not need to be performed in the same configuration as gap based DRS measurements
CSSFwithin_gap,i definition can be reused, both for DRS gap based measurements, and to account for the impact of DRS gap based measurements to other measurements

## Slide 12: Interruptions
The interruption due to transitions between active and non-active during DRX applies in scenario B
The EN-DC interruption due to transitions between active and non-active during DRX is reused in scenario B
The interruption due to PCell transitions from non-DRX to DRX applies in scenario B
The EN-DC interruption due to PCell transitions from non-DRX to DRX is reused in scenario B
The interruption due to Scell addition or release applies in all scenarios A-C
The interruption due to Scell addition or release for an NR-U aggressor cell can reuse the requirements for release 15 NR Scell addition or release
The interruption due to Scell addition or release for an NR-U victim cell can reuse the requirements for release 15 NR Scell addition or release
The interruption due to Scell activation or deactivation applies in all scenarios A-C
The interruption due to Scell activation or deactivation for an NR-U aggressor cell can reuse the requirements for release 15 NR Scell addition or release
The interruption due to Scell activation or deactivation for an NR-U victim cell can reuse the requirements for release 15 NR Scell addition or release
The interruption due to supplementary UL carrier or an UL carrier is configured or de-configured can reuse the requirements for release 15 NR SUL/UL configuration/deconfiguration
If UEs support measurements of NR-U bands with an independent gap pattern, then NR-U operations do not cause interruption to licensed NR cells, nor to LTE cells and vice versa

## Slide 13: Intra-Frequency Measurements Requirements
RAN4 develops NR-U measurements requirements based on NR FR1 requirements which are modified when needed, e.g., to capture the LBT impact
No need in separate scaling factors due to the overlap with measurement gaps or DRS occasions on other intra-frequency NR-U carrier frequencies; the corresponding effects can be captured in CSSF´intra to be defined for NR-U
The time periods TPSS/SSS_sync_intra , TSSB_time_index_intra , and TSSB_measurement_period_intra need to be extended for NR-U to account for L1, L2, and L3 missed DRS occasions, respectively, due to DL LBT, e.g., for non-DRX case on PCell, PSCell, or activated SCell:
T´PSS/SSS_sync_intra =max(600 ms, ceil( (5+L1) x Kp) x DRS period ) x CSSF´intra,
T´SSB_time_index_intra =max(120 ms, ceil( (3+L2) x Kp ) x DRS period) x CSSF´intra ,
T´SSB_measurement_period_intra =max(200 ms, ceil( (5+L3) x Kp) x DRS period) x CSSF´intra .
Maximum allowed values for L1, L2, and L3 are TBD
The requirements shall not apply when the number of consecutively missing DRS occasions is too large. The maximum value is TBD
The intra-frequency cell identification and measurement requirements are defined at least for Es/Iot≥-6 dB

## Slide 14: RLM
RAN4 starts developing NR-U RLM requirements for SSB RLM resources within the DRS window
RLM evaluation periods for NR-U are extended by the number of missing DRS occasions (Lout and Lin for out-of-sync and in-sync, respectively) due to DL LBT failure, e.g., for SSB-based RLM in non-DRX:
  Tevaluate_out = max(200,ceil((10+Lout)*P)*Tssb
  Tevaluate_in = max(200,ceil((5+Lin)*P)*Tssb
Maximum values for Lout and Lin for which the requirements shall apply are TBD
The same target BLER levels are used as a baseline for NR-U and for Rel-15 NR

## Slide 15: RSSI and Channel Occupancy Measurements
The UE needs to be aware of the RSSI and channel occupancy bandwidth, which should preferably be configurable
Configuring the measurement duration and bandwidth shall be independent of the SCS used in the measurement resources, e.g., as fractions or multiples of a subframe and in MHz, respectively, or configured with respect to a reference SCS which may be different from the SCS of the measurement resources
RSSI and channel occupancy measurement resources shall not be limited to SSB time resources or SSB frequencies
Out of the options below, Option 1 (same in LTE) may be used, provided the measured bandwidth is known to the network:
  Option 1: UE reports the measured value, e.g., in dBm (like in LTE)
  Option 2: UE reports a normalized measured value independent on SCS, e.g., dBm per MHz
  Option 3: UE reports a normalized measured value based on SCS, e.g., dBm per SCS or per RB

## Slide 16: SCell Activation Delay
The SCell activation delay in NR-U needs to be extended by accounting for the number of missed SSBs at the UE due to DL LBT failures during Tactivation_time and TCSI_reporting. The maximum acceptable number of such missed SSBs may be limited
The SCell activation delay need to be further extended, by the time reflecting the number of UL LBT failures, if the UE needs to perform UL LBT prior to sending ACK
The known SCell conditions need to be adapted for NR-U by extending the corresponding time periods and imposing the signal level conditions only to the occasions with the present SSBs
The SCell deactivation delay is not impacted by DL LBT failure but may still be impacted by the UE’s UL LBT failure and thus may need to be extended for NR-U compared to NR

## Slide 17: Active TCI State Switching and List Update
The known TCI state definition needs to be updated for NR-U
Failure to transmit ACK due to UL LBT failure may result in disregarding the switching/update command and continuing using the old active TCI state or alternatively in a longer procedure delay (applies to scenarios where the UE transmits ACK on an unlicensed carrier)
Failure to receive DRS due to DL LBT failure, may result in a longer time necessary to complete the active TCI state switching, while extending the procedure by too many DL LBT failures may not be desirable either

## Slide 18: Number of Cells and Beams
On an NR-U intra-frequency carrier frequency, the UE shall be capable of performing intra-frequency measurements for at least the same number of cells and the same number of SSBs as specified for FR1 (TS 38.133)
On an NR-U inter-frequency carrier frequency, the UE shall be capable of performing inter-frequency measurements for at least the same number of cells and the same number of SSBs as specified for FR1 (TS 38.133)
On an NR-U inter-RAT carrier frequency, the UE shall be capable of performing inter-RAT E-UTRANNR measurements for at least the same number of cells and the same number of SSBs as specified for FR1 (TS 36.133)
For UE, which is NR-U capable UE or performing NR-U measurements and which is also performing NR measurements, the existing FR1 and FR2 requirements apply for the measurements on NR (non-NR-U) carriers

## Slide 19: UE Measurement Reporting Criteria
For NR-U intra-frequency RSSI and channel occupancy measurements, Ecat=1 (to be added in TS 38.133)
For NR-U inter-frequency RSSI and channel occupancy measurements, Ecat=1 (to be added in TS 38.133)
For NR-U inter-RAT (E-UTRANNR) RSSI and channel occupancy measurements, Ecat=1 (to be added in TS 36.133)

## Slide 20: Transmit Timing Reference
LAA approach for defining the timing reference within a TAG is not applicable for NR-U
NR-U UE shall support using an activated SCell performing DL LBT as a timing reference for other cells in an sTAG, at least when the sTAG does not contain any SCell not performing DL LBT
NR-U UE shall support using an activated SCell performing DL LBT as a timing reference for other cells in the pTAG, at least in some cases
NR-U UE shall support using an activated SCell performing DL LBT as a timing reference for other cells in the psTAG, at least in some cases

## Slide 21: Other
Discuss whether there is any impact of COT category/configuration on RRM requirements