## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, SI, 26th – 30th August 2019
Huawei, HiSilicon
WF on Rel-16 eMTC RRM
R4-1909697

## Slide 2: DL quality report
The definition of measurement accuracy of DL quality report in Msg3 can re-use from NB-IoT.
RAN4 further waits for RAN1 decision on the MPDCCH parameter for the case where the repetition number in DL quality information equals to 1.
RAN4 further waits for RAN1 decision on where measurement for Msg3 based quality report should be done before defining measurement period.
RAN4 further waits for RAN1 decision on the exact contents of the reporting before discussing the report mapping.

## Slide 3: WUS
Rel-15 WUS requirement metric can be re-used, except that
  99% detection probability applies for each of the WUS sequence UE is monitoring, and
  1% / N false detection probability applies for each of the WUS sequence UE is monitoring.
RAN4 to discuss and decide the assumptions for Rel-16 UE requirements in terms of number of WUS sequences to monitor and the existence of other WUS sequences.

## Slide 4: PUR
It is up to network implementation to use 1 or 2 threshold(s) for RSRP change based TA validation.
Relaxed serving monitoring is allowed when serving cell RSRP change based TA validation is used.
RAN4 should specify the Tx timing requirement for PUR transmission, which should be same as PUSCH transmission in connected mode. RAN4 not to define any synchronization requirement (time to achieve synchronization) related to PUR transmission.

## Slide 5: Mobility enhancement
For RSS based measurement, if requirements are defined,
  measurement period is [5] RSS periods
  requirements are derived based on assumption of 1 or 2 RSS subframe per RSS period
  RAN4 to further discuss the SNR side conditions at which requirements are defined
For relaxed serving monitoring
  when UE is in DRX, the effective interval for serving cell measurement is up to 10.24s
  when UE is in eDRX, the effective interval for serving cell measurement is defined such that UE can complete serving cell monitoring within a PTW