## Slide 1: 29 dBm HPUE SAR and duty cycle
Sprint
3GPP TSG-RAN WG4 Meeting #92
Ljubljana, Slovenia, 26-30 Aug, 2019
R4-1909899

## Slide 2: 29 dBm HPUE SAR restrictions
Sprint previously proposed a 25% duty cycle for 29 dBm HPUE
A question was raised about whether or not SAR was really linear with power
This contribution presents some data that shows for real devices, the SAR is fairly close to being linear with power

## Slide 3: Device 1

## Slide 4: Device 2

## Slide 5: Device 3

## Slide 6: Device 4

## Slide 7: Device 4 (cont.)

## Slide 8: Device 5

## Slide 9: Device 5 (cont.)

## Slide 10: Deivce 6

## Slide 11: Device 6 (cont.)

## Slide 12: Device 7

## Slide 13: Device 7 (Cont.)

## Slide 14: Device 8

## Slide 15: Device 9

## Slide 16: Device 10

## Slide 17: Device 11

## Slide 18: Device 11 (Cont.)

## Slide 19: Device 12

## Slide 20: Device 12 (cont.)

## Slide 21: Device 13

## Slide 22: SAR Linearity Summary
Device | linearity |  |  | 
 | Head | Body Worn | Hotspot | Phablet
1 | -9.92 | -5.63 |  | 
2 | 5.13 |  |  | 
3 | -7.09 |  |  | 
4 | -0.04 | 9.66 | -1.25 | 
5 | -9.59 | -2.1 | -5.79 | 
6 | -8.56 | 6.41 | -9.79 | -9.92
7 | -3.07 | -9.04 | -8.07 | 
8 | -8.78 | -9.49 |  | 
9 | -1.86 |  |  | 
10 | -1.93 | -0.31 |  | 
11 | 0.45 | -4.44 | -1.12 | 
12 | 3.31 | 2.45 | -6.84 | 
13 | -7.04 |  |  | 
average | -3.76846 | -1.38778 | -5.47667 | -9.92
max | 5.13 | 9.66 | -1.12 | -9.92
min | -9.92 | -9.49 | -9.79 | -9.92

## Slide 23: Conclusion
The FCC SAR emission testing samples show that SAR is very close to linear considering power and duty cycle. In all cases the delta was less than 10%.
Therefore, there should be no problem with limiting 29 dBm HPUEs to a 25% duty cycle, just as NR PC2 operation has been limited to less than a 50% duty cycle, and LTE PC2 operation have been restricted to not using LTE configuration 0 or 6.

## Slide 24: Proposal
Proposal 1: RAN4 should agree to use 25% duty cycle as the threshold for enabling/disabling 29 dBm HPUE operation.