## Slide 1: WF on NR MIMO OTA
CAICT
3GPP TSG-RAN WG4 Meeting #92 R4-1909935
Ljubljana, Slovenia, 26-30 Aug, 2019
Agenda item: 11.2.1
Document for: Approval

## Slide 2: Environmental conditions
  The Environmental condition for FR1:
    Continue the discussion on the open issues for UE noise-limited and SNR controlled environmental condition until Nov RAN4 meeting.
    Select one of metrics above by the Nov RAN4 meeting
    SI outcome will recommend the selected metric for test cases metric in the WI phase
  Companies are encouraged to provide measurement results or simulations

## Slide 3: Channel models for NR MIMO OTA
  Down-selection of channel model is agreed
    FR1: UMi CDL-A, Uma CDL-C
    FR2: InO CDL-A, UMi CDL-C

## Slide 4: Test methods for FR1
  Probes configuration
    Option 1: 16 probes with 8 uniformly spaced probes (to guarantee LTE backward compatibility) and remaining 8 probes aligned on a 2D sector for NR FR1
    Option 2: 16 probes ring (uniformly spaced) for NR FR1 MPAC system
  RMS spatial correlation error
    RMS Spatial correlation error of LTE MIMO OTA channel model (i.e. UMi and UMa) is considered as a reference (i.e. the error between ideal channel model correlation and theoretical LTE 8 probes correlation within 1l)
    Use the non-weighted RMS correlation error for NR FR1
  UE vendors are encouraged to study the impact of RMS correlation error on TP performance

## Slide 5: Test methods for FR2
  Measurement distance and PSP
    Focus on 0.75cm and 1m study for corresponding PSP and system dynamic range analysis;
    PSP limit shall be decided next RAN4 meeting;
  Radiated verification of the DL signal EVM per probe is needed for FR2 MIMO OTA.
    A pass-through mode in the fader is needed to verify the EVM under the same waveform scaling conditions that are used when fading emulation is enabled
  Orientations for FR2 MIMO OTA static testing
    Test the UE in FS DML, FS DMP, and FS DSMU as a starting point for FR2, other orientations are not precluded;
      Total azimuthal positions for FR2 static testing is FFS
    Study the vertical rotation for FR2 MIMO OTA;

## Slide 6: NEXT actions
RMS error vs UE throughput or MIMO capacity performance should be studied
Upper limit of RMS error will be decided in next RAN4 meeting
Typical gNodeB emulator setting for FR1 2x2 and 4x4 MIMO shall be studied next meeting