## Slide 1: Way Forward on MR-DC RRM
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #92 R4-1909997
Ljubljana, Slovenia, 26-30 Aug 2019

## Slide 2: MR-DC RRM
Support of asynchronous and synchronous NR-NR Dual Connectivity:
  Background:
    Agreements (RAN4#92):
      RAN4 defines UE requirements for asynchronous inter-band NR-DC
        RAN4 specifies RRM requirements for deployments aligned with agreed band combinations in RF session
      at least if needed RAN4 specifies the following requirements for Rel-16 NR-DC, including MTTD/MRTD, Interruption, PSCell addition, Measurement gap interruption, and SFTD
  Way Forward:
    NR-DC is covered according to WI in RP-191600
    Analyse necessary changes and proposed requirements

## Slide 3: MR-DC RRM
Early Measurement reporting:
  Background:
    Agreements (RAN4#92):
      RAN4 defines measurement requirements for UE early measurement in IDLE and INACTIVE
      RAN4 defines UE requirements for NR Inter-RAT for early measurements
      RAN4 defines UE requirements for LTE Inter-RAT for early measurements
      The supported measurement quantities for early measurements are RSRP and RSRQ
      RAN4 defines measurement accuracy for early measurement reporting
      RAN4 defines measurement period for measurements for early reporting
      RAN4 captures requirements for early reporting based on SIB configuration
      In NR, supporting IDLE/INACTIVE mode CA measurement should not extend the measurement capability defined in Rel-15
  Way Forward:
    Discuss the definition and restriction on carriers for early measurement reporting.
    Discuss if the LTE way of using search thresholds for limiting the UE measurements for idle mode measurements for reporting.
    Analyze the necessary changes and proposed requirements

## Slide 4: MR-DC RRM
Efficient and low latency serving cell configuration, activation and setup:
  Bckground:
    Agreements (RAN4#92):
      RAN4 defines the related UE delay requirements for direct activated configured SCell
      RAN4 defines the interruption requirements for direct SCell activation
      As initial assumption, the direct NR SCell activation delay requirements are based on adapted time lines of corresponding requirements in E-UTRA:
        SCell addition: Ndirect = TRRC_processing + [T1] + Tactivation_time + TCSI_report
        PCell HO: Ndirect = TRRC_processing + Tinterrupt + T2 + T3 + Tinterupt_window + Tactivation_time + TCSI_report
  Way Forward:
    Provide input on whether to replace Tinterupt_window to adapt it to NR requirements
    Provide input on the values for TRRC_processing, T1, Tactivation_time, Tinterrupt, TCSI_report, T2,T3
    Analyze the necessary changes and proposed requirements

## Slide 5: MR-DC RRM
Interruption under EN-DC and NE-DC due to euCA:
  Background:
    Agreements (RAN4#92):
      RAN4 defines requirements for interruptions in EN-DC and NE-DC caused by euCA dormant state and direct SCell activation
  Way Forward:
    Analyze the necessary changes and proposed requirements
    Provide draft CRs

## Slide 6: MR-DC RRM
LS’s to RAN1 and RAN2:
  Agreement:
    Send the LS’s to RAN1 and RAN2
  Drafts have been distributed:
    R4-1909995 Reply LS on maximum allowed SCell activation delay for Rel16 CA
    R4-1909996 [draft] Reply LS on NR fast SCell activation