## Slide 1: WF on UE demodulation requirements with power imbalance
NTT DOCOMO, …
3GPP TSG-RAN WG4 Meeting #92
Ljubljana, Slovenia, 26 – 30 August 2019 Agenda Item: 9.17.1
R4-1910052

## Slide 2: Background
In Rel-10 LTE, RAN4 defined CA PDSCH modulation requirement with 6dB power balance of two adjacent carriers
At the RAN4 #92 meeting, the following proposals were observed for PDSCH demodulation requirements for EN-DC/NR-CA with power imbalance:
Tdoc | Title | Source | Proposal
R4-1908146 | Views on NR CA PDSCH Demodulation Performance Tests | Qualcomm Incorporated | Proposal 1: Define FR1 CA PDSCH demodulation performance test cases under following categories: Regular CA test cases without any power imbalance. Intra-band contiguous CA test cases with power imbalance of 6dB between two carriers. Proposal 2: Do not define FR2 CA PDSCH demodulation performance tests with power imbalance.
R4-1909890 | Power imbalance requirement for intra-band EN-DC/NR CA | DOCOMO Communications Lab. | Proposal 1: Specify the UE demodulation requirement with power imbalance for intra-band EN-DC/NR CA in Rel.16 WI. Detailed simulation assumption is FFS Proposal 2: 6 dB power imbalance is assumed for above requirement as the same level as LTE CA

## Slide 3: Proposal 1/2
Define FR1 CA PDSCH demodulation performance requirement with power imbalance
  Intra-band contiguous 2CC CA with 6dB power imbalance is assumed
Do not define FR2 CA PDSCH demodulation performance requirement with power imbalance
FFS: whether to introduce FR1 EN-DC PDSCH demodulation performance requirement with power imbalance, i.e. 6dB power imbalance between LTE and NR carriers
  Assume 1 CC for LTE and 1 CC for NR
  Assume static channel without extra noise

## Slide 4: Proposal 2/2
The requirement(s) will be specified under the Rel-16 WI of “NR performance requirement enhancement (WID: RP-191587)”, if agreed to be introduced
  Update WID scope accordingly