## Slide 1: Way forward on LTE BS demodulation performance requirements
3GPP TSG-RAN WG4 Meeting #92
Ljubljana, Slovenia, 26th – 30th, Aug 2019
Agenda item: 8.14.4 [LTE_high_speed_enh2-Perf]
Document for: Approval
R4-1910102
NTT DOCOMO, INC.

## Slide 2: Background
In RAN#80, the new WI on further performance enhancement in high speed scenario was approved [1].
In RAN4 #90, the work plan [2] and WF on BS demodulation [3] were approved.
In RAN4 #90bis, WF on BS demodulation [4] was approved.
In RAN4 #91, WF on BS demodulation [5] was approved.
In RAN4 #92, BS performance requirements for high speed were discussed based on contributions [6-11]

## Slide 3: WF on PUSCH for HST
Agreement: Introduce the following new scenarios for HST
Parameter | Value | 
 | Open space | Tunnel for multi-antennas
 | Bi-directional | Bi-directional
Ds | 1000 m | 300 m
Dmin | 50 m | 2 m
v | 500 km/h | 500 km/h
fd | FFS | 

## Slide 4: WF on PUSCH for HST for evaluation
Deployment scenarios and related parameters (e.g., Ds, Dmin, fd) will be decided based on evaluation results. The following parameters should be considered in the evaluation.
Maximum Doppler shift will be based on the outcome of simulation results and could be less than 2 times downlink Doppler shift.
Note: This agreement does not exclude work on unidirectional scenario.
Parameter | Value |  |  | 
 | Open space |  | Tunnel for multi-antennas | 
 | Bi-directional (1st priority) | Uni-directional | Bi-directional (1st priority) | Uni-directional
Ds | 1000 m |  | 300 m | 
Dmin | 50 m |  | 2 m | 
v | 500 km/h |  | 500 km/h | 
fd | 1944 Hz, 1894 Hz, 1844 Hz, 1794 Hz, 1744 Hz, 1694 Hz |  |  | 

## Slide 5: WF on PUSCH for HST for evaluation
Simulation assumption for alignment
Parameters | Unit | Values
Bandwidth | MHz | 10
MCS for PUSCH |  | QPSK 1/3
Propagation condition and correlation matrix |  | Reference to the previous slide
Antenna configuration |  | 1x2
Reference receiver |  | MRC
Noise estimation |  | Practical
Time and frequency track |  | Practical

## Slide 6: WF on PRACH restricted set type B
In RAN4 #90bis, the following agreement was captured in [4].
  After defining maximum Doppler shift, the necessity of a new test case for PRACH restricted set B would be discussed.
Agreement:
  If we adopt maximum Doppler shift more than 1875Hz for PUSCH HST, the new test case with frequency offset equivalent to or more the maximum Doppler shift value to be adopted will be introduced.

## Slide 7: WF on PRACH restricted set type B
Simulation assumption for alignment
  Channel model: AWGN
  Antenna configuration: 1x2
  Frequency offset:
    1944 Hz
    1894 Hz
  Other assumptions are same as existing PRACH restricted set type B requirement

## Slide 8: Reference
[1] RP-181482, “New Work Item on Further performance enhancement for LTE in high speed scenario”, SoftBank, RAN#80
[2] R4-1900804, “Work plan for LTE high speed in Rel.16”, NTT DOCOMO, INC., Huawei, HiSilicon, RAN4#90
[3] R4-1902522, “Way Forward on BS demodulation scenarios and requirements for HST”, Ericsson, NTT Docomo, RAN4#90
[4] R4-1904793, “Way forward on BS demodulation requirement for HST enhancement”, NTT DOCOMO, INC., RAN4#90bis
[5] R4-1907747, “Way forward on LTE HST BS demodulation performance requirements”, Nokia, Nokia Shanghai Bell, NTT DOCOMO, INC., Ericsson, RAN4#91
[6] R4-1908661 BS demodulation for LTE high speed NTT DOCOMO, INC.
[7] R4-1908851 Doppler shift evaluation for LTE HST Bidirectional Scenario Ericsson
[8] R4-1908852 CR to 36.104 on LTE HST PUSCH conditions Ericsson
[9] R4-1909998 Discussion and simulation results for BS performance with HST in LTE Rel-16 Samsung
[10] R4-1909851 Discuss and simulation results for BS demodulation requirements for LTE HST enhancement Huawei, HiSilicon
[11] R4-1909887 BS demodulation simulation results of PUSCH for Rel-16 LTE HST Nokia, Nokia Shanghai Bell