## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, SI, 26th – 30th August 2019
Huawei, HiSilicon, MediaTek, Nokia, Nokia Shanghai Bell, Samsung, Intel, Qualcomm, NTT DOCOMO
WF on RLM test setup
R4-1910104

## Slide 2: Restrictions in T1-T3 in OOS tests
For OOS tests
  T2 > OOS evaluation period (80ms margin)
  D1 = OOS evaluation period + 40ms
  T3 > D1 (40ms margin)
  T310 = 0

## Slide 3: Restrictions in T1-T5 and T310 in IS tests
For IS tests
  T3 > OOS evaluation period (40ms margin)
  T310 > T3 + T4 + IS evaluation period
  D1 > T310 –T3 –T4 + OOS evaluation period + 40ms (40ms margin)
  T5 > D1 (40ms margin)
  T1, T2 and T4 can be small (200ms)
Notes: C+T310 < F
B+OOS +T310 < E+D1
OOS + T310 < T3 + T4 +D1
D1 > T310 + OOS –T3 –T4

## Slide 4: evaluation period for SSB RLM
For A.4.5.1.3,
  Current DRX configuration is DRX.4 which is for LTE
  Propose to change to DRX.3 (40ms DRX cycle)
For A.5.5.1.4,
  Current DRX configuration is DRX.3 with which T310 and D1 satisfying restrictions in Page 2 cannot be found
  Propose to define a new DRX configuration with 20ms DRX cycle

## Slide 5: evaluation period for CSI-RS RLM
For all tests RLM-RS is resource #4 in the TRS resource set
  Check if current TRS configuration in A.3 can be used for RLM
  For FR1, UE is configured with one CORESET, and one TRS resource set which is QCL-ed to the CORESET
  For FR2, UE is configured with two CORESETs, and two TRS resource sets and each is QCL-ed to one CORESET.
For A.4.5.1.7, 4.5.1.8, 5.5.1.7, 5.5.1.8
  Current DRX configuration is DRX.7 (640ms DRX cycle) which leads to very long test time
  Propose to change to DRX.3 (40ms DRX cycle) following FR2 setup
  Propose to add TCI state for CORESET in FR1 RLM tests