## Slide 1: WF for R15 BFR test setup
MediaTek Inc.
3GPP TSG-RAN4 Meeting #92
Ljubljana, Slovenia, 26th – 30th August, 2019
Agenda Item: 7.11.4.8
Document for: Approval
R4-1910105

## Slide 2
  Motivation: Tests shall allow UE to perform fast BFD & CBD.
  Test Requirements
  Before the start of T3, the UE shall not transmit preamble.
  During the period from time point B to time point F, the UE shall transmit preamble on a beam associated with the candidate beam set q1.
Setup for SNR and BFI Counter
  Set SNR level of SSB1 as SNR1 during T3, T4, and T5.
  beamFailureInstanceMaxCount = [n1]
Setup for T1~T5, and D1
  T3 > BFD evlaution period (margin 40ms)
  T2 > BFD evlaution period + CBD evaluation (margin 40ms)
    FFS additional margin of [10] ms
  D1 = CBD evaluation period
    FFS additional margin of [10] ms
  T5>D1 (margin 40ms)
  T1 is small (200 ms), T4=0 ms
BFR test setup

## Slide 3: For information: Configuration setup and BFD/CBD evaluation period (Ref: R4-1909618)
Case | FR | RS type | DRX Config | RS period (ms) | SMTC period (ms) | MGRP (ms) | DRX cycle (ms) | Factor P | Scaling 1.5 | Ptotal | Total Sample Number | Tevaluation
BFD | FR1 | SSB | Non-DRX | 20 | 20 | 40 | N/A | 2 | N/A | 2 | 10 | 200
 |  |  | DRX | 20 | 20 | N/A | 640 | 1 | N/A | 1 | 5 | 3200
 |  | CSI-RS | Non-DRX | 10 | 20 | N/A | N/A | 1 | N/A | 1 | 10 | 100
 |  |  | DRX | 10 | 20 | N/A | 640 | 1 | N/A | 1 | 10 | 6400
 | FR2 | SSB | Non-DRX | 20 | 160 | 40 | N/A | 2 | N/A | 2 | 80 | 1600
 |  |  | DRX | 20 | 160 | N/A | 40 | 8/7 | 3/2 | 12/7 | 69 | 2760
 |  | CSI-RS | Non-DRX | 10 | 160 | N/A | N/A | 16/15 | N/A | 16/15 | 86 | 860
 |  |  | DRX | 10 | 160 | N/A | 40 | 16/15 | 3/2 | 8/5 | 128 | 5120
CBD | FR1 | SSB | Non-DRX | 20 | 20 | 40 | N/A | 2 | N/A | 2 | 6 | 120
 |  |  | DRX | 20 | 20 | N/A | 640 | 1 | N/A | 1 | 3 | 1920
 |  | CSI-RS | Non-DRX | 10 | 20 | N/A | N/A | 1 | N/A | 1 | 3 | 30
 |  |  | DRX | 10 | 20 | N/A | 640 | 1 | N/A | 1 | 3 | 1920
 | FR2 | SSB | Non-DRX | 20 | 160 | 40 | N/A | 2 | N/A | 2 | 48 | 960
 |  |  | DRX | 20 | 160 | N/A | 40 | 8/7 | N/A | 8/7 | 28 | 560
 |  | CSI-RS | Non-DRX | 10 | 160 | N/A | N/A | 16/15 | N/A | 16/15 | 26 | 260
 |  |  | DRX | 10 | 160 | N/A | 40 | 16/15 | N/A | 16/15 | 26 | 260