## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26 - 30 August, 2019
Huawei, HiSilicon
Way forward on NR HST BS demodulation requirements
R4-1910128

## Slide 2: Maximum Doppler shift
Maximum Doppler shift
  Single tap HST 350km/h
    15kHz SCS: 1340Hz
    30kHz SCS: 2334Hz
  Single tap HST 500km/h
    15kHz SCS:
      Option 1: 1944Hz
      Option 2: 1500Hz
      Option 3: 1400Hz
      Option 4: 1250Hz
    30kHz SCS:
      Option 1: 3334Hz
      Option 2: 2600Hz
      Option 3: 3000Hz
      Option 4: 2300Hz

## Slide 3: Channel Model
HST single tap channel model for 350km/h
  Tunnel channel model
  Open space
Parameter | Value
 | Scenario 3
Ds | 300 m
Dmin | 2 m
 | 350km/h
 | 15kHz SCS: 1340Hz 30kHz SCS: 2334Hz
Parameter | Value
 | Scenario 1
(Ds, Dmin) | Option 1: (1000 m, 50m) Option 2: (700 m, 150 m)
v | 350km/h
 | 15kHz SCS: 1340Hz 30kHz SCS: 2334Hz
Option 1 (1000 m, 50m) is baseline for simulation alignment purpose for open space

## Slide 4: Channel Model
HST single tap channel model for 500km/h
  Tunnel channel model
  Open space
Parameter | Value
 | Scenario X
Ds | 300 m
Dmin | 2 m
 | FFS
 | FFS
Parameter | Value
 | Scenario 1
(Ds, Dmin) | Option 1: (1000 m, 50m) Option 2: (700 m, 150 m)
v | FFS
 | FFS
Option 1 (1000 m, 50m)is baseline for simulation alignment purpose for open space

## Slide 5: General
Waveform
  Option 1: CP-OFDM
  Option 2: CP-OFDM and DFT-s-OFDM
SCS
  Option 1: 30kHz
  Option 2: 15kHz and 30kHz
  30kHz targeting for 3.6GHz
  15kHz targeting for 2.1GHz
  Final requirements to be specified will subject to maximum supported Doppler shift based on velocity, operating frequency, NR physical layer design limitation and performance.
CBW
  CP-OFDM
    15kHz SCS
      Option 1: 5/10/20MHz
      Option 2: 20MHz
      Option 3: 10MHz
    30kHz SCS
      Option 1: 10/20/40/100MHz
      Option 2: 40MHz
      Option 3: 10Mhz
  DFT-S-OFDM (If agreed to be introduced)
    Option 1:
      5MHz/15kHz,
      10MHz/30kHz
    Option 2: 10MHz/30kHz

## Slide 6: PUSCH
Reference signal
  Option 1: DMRS (Baseline)
  Option 2: DMRS + PT-RS
    Option 1: 1+1 DMRS + PTRS L=1 or 2
    Other options are not precluded
DMRS Configuration
  For 350km/h targeting velocity, DMRS 1+1+1 (type 1, single-symbol DMRS).
  For 500km/h targeting velocity, FFS on the following DMRS patterns.
    Option 1: 1+1+1 (type 1, single-symbol DMRS)
    Option 2: 2+2 (type 1, double-symbol DMRS)
PUSCH mapping type: type A
l0 for PUSCH mapping type A
  Provide the simulation results for 350km/h and 500km/h and evaluate the following configurations and make decision:
    Option 1: l0 = 3
    Option 2: l0 = 2

## Slide 7: PUSCH
Antenna configuration
  1x2 as baseline for antenna configuration
  FFS on the other configurations
MCS
  Option 1: MCS#2
  Option 2: MCS#16
  Option 3: MCS#2 and MCS#16
Test metric
  Option 1: 70% of maximum throughput
  Option 2: both 30% and 70% of maximum throughput

## Slide 8: UL timing adjustment
Scenarios
  Option 1: (NTT DoCoMo)
  Other options not precluded
Reference signal
  Option 1: SRS for uplink timing advance requirement
  Other options are not precluded
Parameter | Scenario X | Scenario Y | Scenario Z
Channel model | Stationary UE: AWGN Moving UE: TDLC300-400 | Stationary UE: AWGN Moving UE: AWGN | Stationary UE: AWGN Moving UE: AWGN
UE speed | 120 km/h | 350 km/h | 500 km/h
CP length | Normal | Normal | Normal
A | 10*15/SCS μs ,where SCS is Sub Carrier Spacing in kHz. | 10*15/SCS ms ,where SCS is Sub Carrier Spacing in kHz. | 10*15/SCS ms ,where SCS is Sub Carrier Spacing in kHz.
Dw | 0.04 s-1 | 0.13 s-1 | 0.18 s-1

## Slide 9: Way forward
PUSCH demodulation requirements under multi-path fading channel with high Doppler shift is FFS

## Slide 10: PRACH
Channel model
  Option 2: AWGN and TDL-C fading channel
  Option 3: AWGN
PRACH format
  For 350km/h velocity, use PRACH format 0
  For 500km/h velocity, further evaluate PRACH format from 0, A2, A3, B4 and C2.
    Other formats are not precluded for evaluations
Restricted set for PRACH format 0
  Option 1: Type A
  Option 2: Type B
  Option 3: both Type A and Type B
Antenna configuration
  1x2, 1x4 and 1x8
Test metric
  False alarm probability: 0.1%
  missed detection: 99%

## Slide 11: PRACH
Frequency offset under AWGN for PRACH format 0
  Frequency offset for restricted set Type A
    Option 1: 1340Hz with AWGN
    Option 2: 0Hz and 1340Hz with AWGN
  Frequency offset for restricted set Type B
    Option 1: 1944Hz
    Option 2: 1875Hz
    Option 3: 2334Hz
Frequency offset under fading for PRACH format 0
  Frequency offset for restricted set Type A and B
    TDLC300-100 with FO 400 Hz
Frequency offset for PRACH formats with short sequence length targeting 500km/h velocity
  To align with PUSCH maximum Doppler shift
  15kHz SCS
    Option 1: 1944
    Option 2: 1500Hz
    Option 3: 1400Hz
    Option 4: 1250Hz
    Other options are not precluded
  30KhZ SCS
    Option 1: 3334Hz
    Option 2: 2600Hz
    Option 3: 3000Hz
    Option 4: 2300Hz
    Other options are not precluded