## Slide 1: WF on EN-DC power class
Huawei, HiSilicon
R4-1910252
3GPP TSG-RAN WG4 #92
August 26th – 30th, 2019
Ljubljana, SI

## Slide 2: Background
  WF agreed in RAN4 before on EN-DC power class [1].
Option | EN-DC power class | LTE power class | NR Power class
A | PC3 | PC3 | PC3
B | PC2 | PC2 | PC3
C | PC2 | PC3 | PC2
D | PC3 | PC2 | PC3
E | PC3 | PC3 | PC2
F | PC2 | PC2 | PC2
G | PC3 | PC2 | PC2
H | PCX (>PC2) | PC2 | PC2
I | PC2 | PC3 | PC3

## Slide 3: Background
  For EN-DC band combination, only E-UTRA CA power class capability is reported together with the band combination power class capability
BandCombinationList-v1540 ::= SEQUENCE (SIZE (1..maxBandComb)) OF BandCombination-v1540
BandCombination ::= SEQUENCE {
bandList SEQUENCE (SIZE (1..maxSimultaneousBands)) OF BandParameters,
featureSetCombination FeatureSetCombinationId,
ca-ParametersEUTRA CA-ParametersEUTRA OPTIONAL,
ca-ParametersNR CA-ParametersNR OPTIONAL,
mrdc-Parameters MRDC-Parameters OPTIONAL,
supportedBandwidthCombinationSet BIT STRING (SIZE (1..32)) OPTIONAL,
powerClass-v1530 ENUMERATED {pc2} OPTIONAL

## Slide 4: WF
Clear indication of power classes for EN-DC and corresponding E-UTRA and NR bands should be specified in RAN4 Rel-15 specification.
  If LTE or NR has more than one band, the power class for E-UTRA or NR represents CA power class
Send an LS to RAN2 of the agreement on EN-DC power class and ask RAN2 to introduce new per band/CA power class capability under EN-DC band combinations.

## Slide 5: WF
Supported EN-DC power classes from Rel-15 are listed as below.
Option | EN-DC power class | LTE power class | NR Power class
A | PC3 | PC3 | PC3
F | PC2 | PC2 | PC2
I | PC2 | PC3 | PC3

## Slide 6: Reference
[1] R4-1803373, WF on Power Class EN-DC, Qualcomm
[2] R4-1909911, On EN-DC power class, Huawei, HiSilicon