## Slide 1: WF on Region 1 Extension for Power Class 3 Operation in FR2
Skyworks, Nokia, Qualcomm […]
draft_R4-1910280
3GPP TSG-RAN WG4 #92
August 26th – 30th, 2019
Ljubljana, Slovenia

## Slide 2: Background (1/3)
During RAN4#91 and #92, experimental power amplifier back-off measurements indicated that:
  FR2 Inner RB allocations Region 1 for PC3 operation in CBW <= 200 MHz is sub-optimal. Region 1 can be extended [1,2],
  Good agreement between simulation results from [3,4,5] and the measured PA back-off/MPR values [2],
Measurements have been performed with the following RF test conditions:
  Carrier frequency: 24 300 MHz,
  Channel BW = 100 MHz, SCS = 120 kHz
  Modulation: QPSK due to time restrictions
  Waveforms: DFT-S-OFDM and CP-OFDM
  Carrier leakage suppression : -25 dBc, calibrated for each waveform,
  IQ Image suppression: -25 dB, calibrated for each waveform.
Based on correlation between measurements and simulation, [1] proposes to extend Region 1 to an Inner 3rd RB allocation triangle (cf. next slide)

## Slide 3: Background (2/3)
Illustration of Region 1 extension proposal for 100MHz, SCS120kHz [1], QPSK case vs some examples of simulation results [3,4,5]
Source [1]
Source [3]
Source [5]
Source [4]

## Slide 4: Background (3/3)
During RAN4#92, question was raised on the potential impact of Counter-IM3 (C-IM3) products,
Since RAN4 has not agreed on a C-IM3 value for FR2, this document summarizes a way forward on a set of RF impairments for FR2 measurements/simulations and a proposal to extend Region 1.

## Slide 5: Way forward (1/2): Analysis assumption
Agreement 1: Analysis assumptions for FR2 Power Class 3 UE MPR evaluation
Companies are encouraged to evaluate the impact of removing IBE as gating factor to enable power boosting concept [6].
Parameter | Value | Unit | Note
Cell Bandwidth operation | <= 200 | MHz | 
SCS | 120 | kHz | 60kHz SCS not precluded
Waveforms | DFT-S-OFDM |  | 
Modulation scheme | Pi/2 BPSK, QPSK |  | 
Carrier Leakage | -25 | dBc | Output power > 0 dBm
IQ Image | -25 | dB | Output power > 10 dBm
Counter-IM3 | [n-a] | dBc | Companies are invited to evaluate potential impact on emission levels

## Slide 6: Way forward (2/2)
Agreement 2: Evaluate through measurements and/or simulations, the validity of the following Region 1 extension proposal.
For power class 3, BWchannel ≤ 200 MHz operation in FR2, MPR for contiguous allocations is defined as:
MPR = max(MPRWT, MPRnarrow)
where,
  MPRnarrow = 2.5 dB, when the allocated RB size is less than or equal to 1.44 MHz, and 0 ≤ RBstart < Ceil(1/3 NRB) or Ceil(2/3NRB) ≤ RBstart ≤ NRB-LCRB, otherwise MPRnarrow = 0 dB when RB size is greater than 1.44MHz, where NRB is the maximum transmission bandwidth configuration defined in Table 5.3.2-1.
  MPRWT is the maximum power reduction due to modulation orders, transmission bandwidth configurations listed in Table 5.3.2-1, and waveform types. MPRWT is defined in Table 6.2.2.3-1 and Table 6.2.2.3-2.
Where the following parameters are defined to specify valid RB allocation ranges for RB allocations in Tables 6.2.2.3-1 and 6.2.2.3-2:
  RBStart,Low = max(1, LCRB), where max() indicates the largest value of all arguments.
  RBStart,High = NRB – RBStart,Low – LCRB,
An RB allocation belonging to table 6.2.2.3-1 is a Region 1 inner RB allocation if:
  RBStart,Low ≤ RBStart ≤ RBStart,High, and LCRB ≤ ceil(NRB/3), where ceil(x) is the smallest integer greater than or equal to x.
An RB allocation is an Edge allocation if it is NOT a Region 1 inner allocation.

## Slide 7: References
[1] R4-1909945 Inner RB Allocations Region 1 Extension for Power Class 3 Operation in FR2, R4 #92, Skyworks Solutions Inc.
[2] R4-1907163 FR2 PC3 MPR PA Measurements for DFT-S-OFDM and CP-OFDM for Rel-16, R4 #91, Skyworks Solutions Inc.
[3] R4-1903524 FR2 MPR due to OBW, R4 #90 bis Xi’an China, Nokia, Nokia Shanghai Bell .
[4] R4-1902848 On FR2 PC1 MPR and OBW, R4 #90 bis Xi’an China, Qualcomm.
[5] R4-1902930 On PC1 MPR and CA MPR, R4 #90 bis Xi’an China, Intel.
[6] R4-1909927 Power Boost and IBE in FR2, R4 #92 Ljubljana, Slovenia, Qualcomm.