## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, SI, 26th – 30th August 2019
Qualcomm Incorporated, …
Performance Difference between Different SSB Locations in NR-U
R4-1910389

## Slide 2: SSB in Center of sub-band
RAN1 perspective:
  Non continuous RBs available to carry SIB1 in RMSI PDSCH:
    RMSI PDSCH cannot currently rate-match around SSB
      Rate matching behavior will have to be defined
      Other options (resource allocation with discontinuous RBs, smaller RMSI size) can also be explored but will have specification impact
  CSI-RS cannot be FDM’ed with SSB unless specification is modified (i.e., non-contiguous CSI-RS or CSI-RS rate matching)
    NOTE: RAN1 agreed CSI-RS can be transmitted together with SSB to fulfil OCB requirements.
RAN4 perspective:
  Similar impact of adjacent channel interference on SSS detection performance when the SSB is placed at the edge of sub-band or in the center of sub-band
Proponents: Nokia, Huawei, OPPO

## Slide 3: SSB in Edge of sub-band
RAN1 perspective:
  Continuous RBs available to carry SIB1 in RMSI PDSCH:
    RMSI PDSCH rate-matching around SSB is not needed
  CSI-RS can be FDM’ed with SSB without specification impact
    NOTE: RAN1 agreed CSI-RS can be transmitted together with SSB to fulfil OCB requirements.
RAN4 perspective:
  Similar impact of adjacent channel interference on SSS detection performance when the SSB is placed at the edge of sub-band or in the center of sub-band
Proponents: Qualcomm, Ericsson, MediaTek, LGE, Charter