## Slide 1: WF on Guardbands for NR-U
Nokia
R4-1910386
3GPP TSG-RAN WG4 #92
August 26th – 30th, 2019
Ljubljana, Slovenia

## Slide 2: Definition of Guardbands for Wideband Operation
  Based on discussions related to R4-1908559, R4-1909259, R4-1908716, R4-1909202 and R4-1908985 there is consensus to:
  -> Define two different types of guardbands for NR-U:
    Carrier guardbands (inter-carrier guardbands)
    In-carrier guardbands (intra-carrier guards)

## Slide 3: Definition of Guardbands for Wideband Operation
  -> Intra-carrier guards for a carrier configured by a serving cell are defined as an integer number of full PRBs.
  - These are defined on a common RB grid which reference point is configured by the gNB as specified in section 5.3.4 of 38.101-1.
  - No intra-carrier guards are defined for 20 MHz carriers
  -> RAN4 is tasked to specify necessary sizes of the inter-carrier guardbands and number of PRBs needed for intra-carrier guards to meet spectral emission mask defined for NR-U.
  -> The intra-carrier guard band could be scheduled if it is located within the adjacent contiguous LBT successful sub-bands where all scheduled LBT sub-bands have passed. Introduction of flexible guard-bands at sub-block edge is left FFS. Meaning scheduling of either additional or a reduced number of sub-block edge guard PRBs.