## Slide 1: WF on RRM Requirements for NR-U
Ericsson, Qualcomm Inc., Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #92 R4-1910551
Ljubljana, Slovenia, 26th – 30th August 2019
Agenda Item: 9.1.5

## Slide 2: Serving Cell Evaluation
The NR-U standalone UE shall measure and evaluate the cell selection criterion S for the serving cell at least once every (1+Ms)*M1 DRX cycles in Nserv consecutive DRX, where
  M1 value
    M1=2 if DMTC periodicity (TDMTC) > TBD and DRX cycle ≤ 0.64 second, otherwise M1=1
  Nserv is as defined below
Maximum value of Ms is TBD
DRX cycle length [s] | Nserv [number of DRX cycles]
0.32 | M1*4 + M1*Ms
0.64 | M1*4 + M1*Ms
1.28 | 2 + Ms
2.56 | 2 + Ms

## Slide 3: Serving Cell Evaluation (cont.)
The UE shall restart the measurements used for serving cell evaluation if it cannot fulfil the conditions on the maximum value of Ms
  FFS how to determine the maximum value of Ms
  The UE behavior needs be clarified
UE shall initiate measurements on neighbour cells indicated by the serving cell if it is unable to measure on the serving cell for at least Mp consecutive number of DRX cycles not available at the UE, where the value of Mp is TBD
UE shall initiate the measurements on neighbour cells of any intra-frequency or inter-frequency if it is unable to measure on serving cell during at least consecutive Mq number of DRX cycles not available at the UE, regardless of any condition of SnonIntraSearchP and SnonIntraSearchQ

## Slide 4: Cell Reselection
NR-U standalone cell re-selection requirements to the target intra- and inter-frequency NR-U cell are as defined below:
where Md, Mm, Me are the number of DMTC occasions not available at the UE during the corresponding time periods
Maximum values of Md, Mm, and Me are TBD
  UE behavior: restart the measurements if the limits are exceeded
Measurement requirements in RRC_IDLE on non-NR-U inter-frequency and inter-RAT LTE shall follow the existing requirements for UE camping on an NR-U cell. The impact of DL LBT in the serving cell on cell reselection procedure is FFS
The UE shall filter the measurement (e.g. SS-RSRP/SS-RSRQ) using at least 2 measurements which are separated in time by at least DRX/2 but not separated in time by more than Mn. Mn is number of DRX cycles not available at the UE. FFS whether Mn depends on DRX cycle length
Inclusion of SI reading in cell reselection requirements
  Postpone the discussion until/if the procedure is agreed in RAN2
DRX cycle length [s] | Tdetect,NR_Intra , Tdetect,NR_Inter [s] {number of DRX cycles} | Tmeasure,NR_Intra, Tmeasure,NR_Inter [s] {number of DRX cycles} | Tevaluate,NR_Intra, Tevaluate,NR_Intra [s] {number of DRX cycles}
0.32 | 0.32x([36]+Md)xM2 {([36]+Md)xM2} | 0.32x([4]+Mm) xM2 {([4]+Mm)xM2} | 0.32x([16]+Me) x M2 {([16]+Me)xM2}
0.64 | 0.64x([28]+Md) {[28]+Md} | 0.64x([2]+Mm) {[2]+Mm} | 0.64x([8]+Me) {[8]+Me}
1.28 | 1.28x([25]+Md) {[25]+Md} | 1.28x([1]+Mm) {[1]+Mm} | 1.28x([5]+Me) {[5]+Me}
2.56 | 2.56x([23]+Md) {[23]+Md} | 2.56x([1]+Mm) {[1]+Mm} | 2.56x([3]+Me) {[3]+Me}

## Slide 5: Handover
SI reading in HO requirements
  Postpone the discussion until/if the procedure is agreed in RAN2
The interruption time for NR FR1 – NR FR1 handover in NR-U:
Tinterrupt = Tsearch + TIU + [20] + ms
where
Tsearch is the time required to search the target cell when the target cell is not already known when the handover command is received by the UE. If the target cell is known, then Tsearch = 0 ms. If the target cell is an unknown intra-frequency cell and the target cell Es/Iot≥[-2] dB, then Tsearch = (1+ L1)* Trs + 2 ms. If the target cell is an unknown inter-frequency cell and the target cell Es/Iot≥[-2] dB, then Tsearch = [(3+ L1´)* Trs + 2] ms where L1 and L1´ is the number of DRS occasions missed due to DL LBT during the intra-frequency and inter-frequency detection period, respectively.
T∆ is the time for fine time tracking and acquiring full timing information of the target cell. T∆ = (1+ L2) * Trs ms where L2 is the number of DRS occasions missing at the UE due to DL LBT during the time tracking period.
TIU is the interruption uncertainty in acquiring the first available PRACH occasion in the new cell. TIU can be up to: (1 + L3) * TSSB,RO + 10 ms where TSSB,RO is the SSB to PRACH occasion association period [3] and L3 is the number of PRACH occasions that are unavailable for PRACH transmission due to LBT failure.
Trs is the DRS periodicity of the target NR cell, details are FFS.
L1≤ L1,max, L´1≤ L´1,max, L2≤ L2,max, L3≤ L3,max, and the maximum values Li,max are TBD.
FFS on UE behavior when L1 > L1,max, L´1 > L´1,max, L2> L2,max, or L3> L3,max.

## Slide 6: Active BWP Switching
The basic time period over which the BWP switching occurs shall be the same as defined in the existing requirements (applies for DCI-, timer-, and RRC-based active BWP switching)
The impact of LBT failures on PDSCH reception or PUSCH transmission after the BWP switching needs further investigation
The duration of interruption on a serving cell in licensed band or unlicensed band or due to BWP switching on a licensed or unlicensed band can be based on the existing interruption requirements

## Slide 7: RRC Release with Redirection
For the cases NR-UNR-U and NRNR-U, extend in RRC release with redirection requirements:
  Tidentify-NR to account for DL LBT
  TSI-NR to account for DL LBT
  TPRACH to account for UL LBT
Tidentify-NR is as follows:
Maximum allowed value of L1 is TBD. L1 is the number of DMTC cycles not available at the UE
Frequency range (FR) of target NR cell | Tidentify-NR
FR1 | MAX (680 ms, ([11] + L1) x TDMTC)

## Slide 8: RRC Release with Redirection (cont.)
TPRACH for NR-U is defined by scaling Rel-15 TPRACH by (1+L2), L2 is the number of missed PRACH occasions due to UL LBT. The maximum value of L2 is TBD.
Existing (NRNR) requirements apply for the case NR-U NR
Existing (NRLTE) requirements apply for the case NR-U LTE, provided the procedure is supported

## Slide 9: RRC Re-Establishment
For the cases NR-UNR-U and NRNR-U, extend in RRC re-establishment requirements:
  Tidentify_intra_NR and Tidentify_inter_NR,i to account for DL LBT,
  TSI-NR to account for DL LBT, and
  TPRACH to account for UL LBT
TPRACH for NR-U is defined by scaling Rel-15 TPRACH by (1+K3), K3 is the number of PRACH occasions that are unavailable for PRACH transmission due to UL LBT failure. Maximum value for K3 is TBD.
Existing requirements for RRC Re-establishment apply for the case NR-U NR

## Slide 10: RRC Re-Establishment (cont.)
Tidentify_intra_NR is as follows:
Maximum allowed value of K1 is TBD. K1 is the number of DMTC cycles not available at the UE
NOTE: The requirement above is per target cell
Tidentify_inter_NR, i is as follows:
Maximum allowed value of K2,i is TBD. K2,i is the number of DMTC cycles not available at the UE
NOTE: The requirement above is per target cell
Serving cell SSB Ês/Iot (dB) | Frequency range (FR) of target NR cell | Tidentify_intra_NR [ms] | 
 |  | Known NR cell | Unknown NR cell
≥ [-8] | FR1 | MAX (200 ms, ([5]+K1) xTDMTC) | MAX (800 ms, ([10]+K1) x TDMTC)
< [-8] | FR1 | N/A | (800+TBD*K1)Note1
Note 1: The UE is not required to successfully identify a cell on any NR frequency layer when TDMTC > TBD ms and serving cell SSB Ês/Iot < [-8] dB. |  |  | 
Serving cell SSB Ês/Iot (dB) | Frequency range (FR) of target NR cell | Tidentify_inter_NR, i [ms] | 
 |  | Known NR cell | Unknown NR cell
≥ [-8] | FR1 | MAX (200 ms, ([6]+K2,i)xTDMTC, i) | MAX (800 ms, ([13]+K2,i) x TDMTC, i)
< [-8] | FR1 | N/A | (800 + TBD*K2,i)Note1
Note 1: The UE is not required to successfully identify a cell on any NR frequency layer when TDMTC,i > TBD ms and serving cell SSB Ês/Iot < [-8] dB. |  |  | 

## Slide 11: Beam Management
Evaluation time for BFD is as follows, where the maximum value for LBFD is TBD:
Evaluation time for CBD is as follows, where the maximum value for LCBD is TBD:
Configuration | TEvaluate_BFD_SSB (ms)
no DRX | max([50], ceil((5+LBFD)*P)*TDRS)
DRX cycle ≤ 320ms | max([50], ceil((7.5+LBFD)*P)*max(TDRX,TDRS))
DRX cycle > 320ms | ceil((5+LBFD)*P)*TDRX
NOTE 1: TDRS is the periodicity of DRS in the set . TDRX is the DRX cycle length. NOTE 2: LBFD is the total number of missed DRS occasions due to LBT. | 
Configuration | TEvaluate_CBD_SSB (ms)
non-DRX, DRX cycle ≤ 320ms | ceil(([3]+LCBD)*P) * TDRS
DRX cycle > 320ms | ceil(([3]+LCBD)*P) * TDRX
NOTE 1: TDRS is the periodicity of DRS in the set . TDRX is the DRX cycle length. NOTE 2: LBFD is the total number of missed DRS occasions due to LBT. | 

## Slide 12: Beam Management (cont.)
The same frameworks as for NR beam management requirements (e.g., L1-RSRP and BFD) can be used as the start point in RAN4 RRM study until RAN1&2 updates

## Slide 13: L1-RSRP measurements
Measurement period for SSB-based L1-RSRP:
Measurement period for CSI-RS based L1-RSRP:
Note: the above can be revisited when RAN1 design is finalized
Configuration | TL1-RSRP_Measurement_Period_SSB (ms)
non-DRX | max(TReport, ceil((M+L1)*P)*TSSB)
DRX cycle ≤ 320ms | max(TReport, ceil(1.5*(M+L1)*P)*max(TDRX,TSSB))
DRX cycle > 320ms | ceil((M+L1)*P)*TDRX
Note: TSSB is the periodicity of the SSB-Index configured for L1-RSRP measurement. TDRX is the DRX cycle length. TReport is configured periodicity for reporting. | 
Configuration | TL1-RSRP_Measurement_Period_CSI-RS (ms)
non-DRX | max(TReport, ceil((M+L2)*P)*TCSI-RS)
DRX cycle ≤ 320ms | max(TReport, ceil(1.5*(M+L2)*P)*max(TDRX,TCSI-RS))
DRX cycle > 320ms | ceil((M+L2)*P)*TDRX
Note 1: TCSI-RS is the periodicity of CSI-RS configured for L1-RSRP measurement. TDRX is the DRX cycle length. TReport is configured periodicity for reporting. Note 2: the requirements are applicable provided that the CSI-RS resource configured for L1-RSRP measurement is transmitted with Density = 3. | 

## Slide 14: L1-RSRP measurements (cont.)
Define maximum values for L1 and L2
SSB based L1-RSRP measurement reporting is performed only when UE receives MSSB SSB samples during the measurement period
CSI-RS based L1-RSRP measurement reporting is performed only when UE receives MCSi-RS CSI-RS samples during the measurement period
If the UE cannot skip the L1-RSRP reporting, but the UE does not receive a certain number of SSB and/or CSI-RS samples within the measurement period, the UE indicates ‘not valid’ (how to signal “not valid” is FFS)

## Slide 15: Measurement Gaps: Applicability
Gap patterns with MGL=6ms are suitable for measurements based on DRS
MG patterns #0 and #1 for measurements based on DRS are mandatory
The requirements with MG pattern #5 will be specified
FFS on MG pattern #4 depending on the DMTC periodicity and #5
No new MG pattern needs to be introduced for DRS based measurements

## Slide 16: Measurement Gaps: Scaling Factor
Interested companies are invited to provide their analysis in RAN4#92-Bis on the feasibility of a capability to measure NR-U bands with an independent gap pattern
CSSFwithin_gap,i definition can be reused, both for DRS gap based measurements, and to account for the impact of DRS gap based measurements to other measurements. DMTC period in the definition is to be used instead of SMTC period.

## Slide 17: Interruptions
The interruption due to transitions between active and non-active during DRX applies in scenario B
  The EN-DC interruption due to transitions between active and non-active during DRX is reused in scenario B
The interruption due to PCell transitions from non-DRX to DRX applies in scenario B
  The EN-DC interruption due to PCell transitions from non-DRX to DRX is reused in scenario B
The interruption due to Scell addition or release applies in all scenarios A-C
  The interruption due to Scell addition or release for an NR-U aggressor cell can reuse the requirements for release 15 NR Scell addition or release
  The interruption due to Scell addition or release for an NR-U victim cell can reuse the requirements for release 15 NR Scell addition or release

## Slide 18: Interruptions (cont.)
The interruption due to SCell activation or deactivation applies in all scenarios A-C
  The interruption due to SCell activation or deactivation for an NR-U aggressor cell can reuse the requirements for release 15 NR SCell addition or release
  The interruption due to Scell activation or deactivation for an NR-U victim cell can reuse the requirements for release 15 NR SCell addition or release
The interruption due to supplementary UL carrier or an UL carrier is configured or de-configured can reuse the requirements for release 15 NR SUL/UL configuration/deconfiguration
The deactivation interruption on PCell or PSCell or any activated SCell shall not occur before slot n+1+[THARQ] and not occur after slot n+1+[THARQ +3ms]
  The definition of T_HARQ needs be clarified

## Slide 19: Intra-Frequency Measurements (RSRP, RSRQ, SINR)
The intra-frequency cell identification and measurement requirements are defined for Es/Iot≥-6 dB
FFS: UE behavior for the case when the maximum value (e.g., for LPSS/SSS or Lmeas) is exceeded

## Slide 20: Intra-Frequency Measurements (RSRP, RSRQ, SINR) (cont.)
Cell identification and measurement periods without gaps are as follows:
Define maximum values for L-values in the above
Note: CSSF for NR-U is being discussed separately
Note: the same approach is applicable for SSB index identification, unless RAN2 defines a different procedure
Note: the above can be revisited when RAN1 design is concluded
DRX cycle | TPSS/SSS_sync_intra_NR_U
No DRX | max( 600ms, ceil((5+LPSS/SSS) x Kp) x DMTC period )Note 1 x CSSFintra
DRX cycle≤ 320ms | max( 600ms, ceil(1.5x (5+LPSS/SSS) x Kp) x max(DMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | ceil((5+LPSS/SSS) x Kp) x DRX cycle x CSSFintra
DRX cycle | (for deactivated SCell) TPSS/SSS_sync_intra_NR_U
No DRX | (5 + LPSS/SSS) x measCycleSCell x CSSFintra
DRX cycle≤ 320ms | (5 + LPSS/SSS) x max(measCycleSCell, 1.5xDRX cycle) x CSSFintra
DRX cycle> 320ms | (5 + LPSS/SSS) x max(measCycleSCell, DRX cycle) x CSSFintra
DRX cycle | T SSB_measurement_period_intra_NR_U
No DRX | max(200ms, ceil( (5+Lmeas) x Kp) x DMTC period)Note 1 x CSSFintra
DRX cycle≤ 320ms | ma(200ms, ceil(1.5x (5+Lmeas) x Kp) x max(DMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | ceil( (5+Lmeas) x Kp ) x DRX cycle x CSSFintra

## Slide 21: Intra-Frequency Measurements (RSRP, RSRQ, SINR) (cont.)
Cell identification and measurement periods with gaps are as follows:
Define maximum values for L-values in the above
Note: CSSF for NR-U is being discussed separately
Note: the same approach is applicable for SSB index identification, unless RAN2 defines a different procedure
Note: the above can be revisited when RAN1 design is concluded
DRX cycle | TPSS/SSS_sync_intra_NR_U
No DRX | max(600ms, (5 + LPSS/SSS) x max(MGRP, DMTC period)) x CSSFintra
DRX cycle≤ 320ms | max(600ms, ceil(1.5x(5+LPSS/SSS)) x max(MGRP, DMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | (5 + LPSS/SSS) x max(MGRP, DRX cycle) x CSSFintra
DRX cycle | T SSB_measurement_period_intra_NR_U
No DRX | max(200ms, (5 + Lmeas) x max(MGRP, DMTC period)) x CSSFintra
DRX cycle≤ 320ms | max(200ms, ceil(1.5x(5+Lmeas)) x max(MGRP, DMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | (5 + Lmeas) x max(MGRP, DRX cycle) x CSSFintra

## Slide 22: Inter-Frequency Measurements (RSRP, RSRQ, SINR)
For inter-frequency, use the same approach as for intra-frequency:
Define maximum values for L-values in the above
Note: CSSF for NR-U is being discussed separately
Note: the same approach is applicable for SSB index identification, unless RAN2 defines a different procedure
Note: the above can be revisited when RAN1 design is concluded
Condition | TPSS/SSS_sync_inter_NR_U
No DRX | max(600ms, (8+LPSS/SSS) x max(MGRP, DMTC period)) x CSSFinter
DRX cycle ≤ 320ms | max(600ms, ceil((8+LPSS/SSS)x1.5) x max(MGRP, DMTC period, DRX cycle)) x CSSFinter
DRX cycle > 320ms | (8 + LPSS/SSS) x DRX cycle x CSSFinter
Condition NOTE1,2 | T SSB_measurement_period_inter_NR_U
No DRX | max(200ms, (8 + Lmeas) x max(MGRP, DMTC period)) x CSSFinter
DRX cycle ≤ 320ms | max(200ms, ceil((8+Lmeas) x 1.5) x max(MGRP, DMTC period, DRX cycle)) x CSSFinter
DRX cycle > 320ms | (8 + Lmeas) x DRX cycle x CSSFinter

## Slide 23: Inter-RAT Measurements
Existing requirements shall apply to inter-RAT measurements in NR-U if the RAT being measured is in licensed band. When RAT being measured is NR-U (Scenario B before PSCell add), inter-RAT measurement requirements can be based on inter-frequency NR-U measurement requirements

## Slide 24: SFTD Measurements
For EN-DC SFTD towards NR-U with LBT, a measurement period Tmeasure_SFTD1 = max(0.2,[5 + NLBT-fail] x SMTC period), where NLBT-fail is the number of SSBs (or DRSs) that have been blocked by LBT, is used
For EN-DC SFTD towards NR-U with LBT, SFTD measurement accuracy under LBT shall be safe-guarded by limiting the time between acquisition of PCell timing and acquisition of PSCell timing used when estimating SFTD. One option may e.g. be to request that |t1-t2| < SMTC period, another to request that |t1-t2| < max(0.2, 5xSMTC period)
RAN4 shall further discuss how to capture measurement delay requirements for inter-RAT SFTD towards NR-U under LBT
Extension of SFTD measurement time when PSCell changes without changing carrier frequency to be similar to the described way in clause 8.17.2 of TS 36.133

## Slide 25: SFTD (cont.)
For EN-DC, the SFTD measurement period towards NR-U with LBT under DRX:
Define the maximum value of L
  FFS UE behavior when the maximum is exceeded
DRX cycle length (s) | T measure_SFTD1_NR_U
≤0.04 | max(200ms, (5 + L) x DMTC period)) (Note 1)
DRX cycle ≤ 320ms | (L + 8) x max(DRX cycle, DMTC period)
DRX cycle > 320ms | (L + 5) x DRX cycle
Note 1: Number of DRX cycles depends upon the DRX cycle in use Note 2: DRX cycle length in this table refers to the DRX cycle length configured for PCell or PSCell. When DRX is used in both PCell and PSCell, DRX cycle length in this table refers to the longer of the DRX cycle lengths for PCell and PSCell. | 

## Slide 26: RLM
The same target BLER levels are used as a baseline for NR-U and for Rel-15 NR
Define the NR-U RLM requirements for SSB RLM resources within DRS window
RAN4 does not work on RLM requirements for any new RLM metric, unless RAN1 decides to define such
In-sync evaluation period:
Maximum value of Lin is TBD
Configuration | TEvaluate_in_SSB (ms)
no DRX | max(100,ceil((5+Lin)*P)*TSSB)
DRX cycle≤320 | max(100,ceil((7.5+Lin)*P)*max(TDRX,TSSB))
DRX cycle>320 | ceil((5+Lin)*P)*TSSB
NOTE 1: TSSB is the periodicity of SSB RLM-RS configured for RLM. TDRX is the DRX cycle length. | 

## Slide 27: RSSI and Channel Occupancy Measurements
FFS: The resource configuration for RSSI/channel occupancy shall be independent of the SCS used e.g., for data
Both the network and UE need to be aware of the RSSI measured bandwidth

## Slide 28: SCell Activation Delay
The SCell activation delay in NR-U needs to be extended by accounting for the number of missed SSBs at the UE due to DL LBT failures during Tactivation_time and TCSI_reporting
The maximum acceptable number of missed SSBs due to LBT is TBD
The known SCell definition needs to be updated for NR-U
The SCell activation delay needs to be further extended, by the time reflecting the number of UL LBT failures, if the UE needs to perform UL LBT prior to sending ACK

## Slide 29: Active TCI State Switching and List Update
The known TCI state definition needs to be updated for NR-U
Failure to receive DRS due to DL LBT failure, results in a longer time necessary to complete the active TCI state switching
In the TCI requirements limit the maximum acceptable number of missed DRS occasions due to LBT
  FFS on UE behavior if the maximum acceptable number is exceeded
Failure to transmit ACK due to UL LBT failure (when the ACK is transmitted on unlicensed carrier) may result in a longer procedure delay due to UE re-attempt to transmit

## Slide 30: PSCell Addition / Release
The PSCell release delay is not subject to signal availability and the existing requirements in 7.31 of 36.331 should apply

## Slide 31: Number of Cells and Beams
On an NR-U intra-frequency carrier frequency, the UE shall be capable of performing intra-frequency measurements for at least the same number of cells and the same number of SSBs as specified for Rel-15 FR1 (TS 38.133)
On an NR-U inter-frequency carrier frequency, the UE shall be capable of performing inter-frequency measurements for at least the same number of cells and the same number of SSBs as specified for Rel-15 FR1 (TS 38.133)
On an NR-U inter-RAT carrier frequency, the UE shall be capable of performing inter-RAT E-UTRAN–NR measurements for at least the same number of cells and the same number of SSBs as specified for Rel-15 FR1 (TS 36.133)
For UE, which is NR-U capable UE or performing NR-U measurements and which is also performing NR (non-NR-U) measurements, the existing FR1 and FR2 requirements apply for the measurements on NR (non-NR-U) carriers

## Slide 32: UE Measurement Reporting Criteria
Reporting criteria, at least for the case when the bandwidth is up to 20 MHz:
  For NR-U intra-frequency RSSI and channel occupancy measurements, Ecat=1 (to be added in TS 38.133)
  For NR-U inter-frequency RSSI and channel occupancy measurements, Ecat=1 (to be added in TS 38.133)
  For NR-U inter-RAT (E-UTRANNR) RSSI and channel occupancy measurements, Ecat=1 (to be added in TS 36.133)

## Slide 33: Timing Requirements
MRTD and MTTD requirements in NR-U networks are same as those of Rel-15 requirements

## Slide 34: Other
Discuss whether there is any impact of COT category/configuration on RRM requirements