## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26th – 30th Aug 2019
Huawei, HiSilicon,…
Way forward on RRM impact of the R16 enhancement for NB-IoT
R4-1910569

## Slide 2: Group WUS
Release 15 WUS framework is used to evaluate the release 16 WUS performance.
  Companies are expected to analyse the WUS detection performance of each WUS sequence assuming UE monitors two sequences based on Rel-15 WUS framework in R4-1816334.
  The simulation assumptions will be updated if necessary.

## Slide 3: Preconfigured UL resource 1/2
Both in serving cell relaxed monitoring mode and in serving cell non-relaxed monitoring mode, if UE is configured with RSRP change for TA validation, the first and the second measurements used for validating the TA shall satisfy the following conditions
    The first measurement (NRSRP1) shall be performed within following time range: T1 – N ≤ T1’ ≤ T1 + N;
    The second measurement (NRSRP2) shall be performed within following time range: T2 – M ≤ T2’<T2;
    Where T1’ is the time when NRSRP1 becomes available, T1 is the time when TA is obtained, N is TBD, T2’ is the time when RSRP2 becomes available, T2 is the time when TA is validated, M TBD.
Relaxation on serving cell monitoring is allowed regardless of TA validation mechanism.

## Slide 4: Preconfigured UL resource 2/2
eNB can configure the UE with any of K=1 and K=2, i.e. one or two thresholds for validating the TA when configured with serving cell measurement change attribute.

## Slide 5: Multi carrier operation MSG3 based quality reporting
Use evaluation period T2 if quality report is associated with non-anchor carrier.

## Slide 6: Multi carrier operation non-anchor RRM
For RRM measurements on non-anchor carriers based on NRS
  Skip the NRSRQ measurement on non-anchor carrier.
  The existing criteria depending on NRSRQ are not feasible on non-anchor carrier.
  It is left to RAN2 whether to modify the existing S criteria or define new criteria.

## Slide 7: Multi carrier operation connected channel quality report
Use the same hypothetical NPDCCH parameters, report mapping and accuracy requirements as MSG3-based report.
UE can use the NPDCCH period which carries the UL grant of channel quality report for measurement of DL channel quality of the configured carrier. Per TS 36.213, the NPDCCH repetition level can be from the set